## Slide 1: UECS1013 Introduction to Computer Organisation and Architecture
Lecture 4

## Slide 2: Outline: Digital Logic Design
  Logic Gates
    The Basic Logic Gates
  Representing a Circuit Using Boolean Functions
    Truth Table
    Boolean Expression
  Truth Table  Boolean Expression  Circuit
    Sum of MinTerm
    Product of Maxterm
  Simplifying Boolean Function
    Boolean Algebra
    K-MAP

## Slide 3: THE BASIC LOGIC GATES

## Slide 4: Logic Gates
A logic gate is the smallest processing unit in a digital system. It takes one or a few bits as input and generates one bit as output.
A digital circuit is formed by applying the outputs of gates to the input of other gates. It takes a group of bits as input and generates one or more bits as output.
For example, an 8-bit adder takes two 8-bit binary numbers and computes their sum in its 9-bit outputs. We say that the adder is computing an addition function.
A computer can be viewed as a giant circuit computing certain complex function.

## Slide 5: Logic Gates
Gate Symbols
EXCLUSIVE OR
a
b
a.b
a
b
a+b
a
a'
a
b
(a+b)'
a
b
(a.b)'
a
b
a  b
a
b
a.b
&
a
b
a+b
1
AND
a
a'
1
a
b
(a.b)'
&
a
b
(a+b)'
1
a
b
a  b
=1
OR
NOT
NAND
NOR
Symbol set 1
Symbol set 2
(ANSI/IEEE Standard 91-1984)

## Slide 6: The OR Gate
A
B
A+B
2 input OR gate
3 input OR gate
A
B
C
A+B+C
Similar to a parallel set of switches
Outputs a 1 if at least one of the inputs is 1. Outputs a 0 otherwise.
Number of inputs can be more than 3 but will cause delay
Example application: to trigger the alarm if any window is opened

## Slide 7: The AND Gate
A
B
A.B
Similar to a series set of switch
Outputs a 1 if all inputs are 1, and outputs a 0 otherwise.
Number of inputs can be more than 3 but will cause delay
2 input AND gate
3 input AND gate
A
B
C
A.B.C

## Slide 8: The AND Gate
Example application: as an enable feature
1 sec
A
1 sec
Enable
A
Enable
Counter
Reset to zero between Enable pulses
Register, decode and frequency display

## Slide 9: The Inverter
A
A'
A
A'
  Takes a bit X and outputs a 1 if X is 0, and outputs a 0 otherwise.
Only takes in one input
Example application: 1’s Complement
1
0
0
1
0
1
0
1
1
0
0
1
1
0
1
0
Binary number
1’s Complement

## Slide 10: The NAND Gate
A
B
(A.B)'
A
B
(A.B)'

NAND
Negative-OR

Outputs a 0 if all inputs are 1, and outputs a 1 otherwise.
A nand can be constructed using two inverters and an OR gate
3 input NAND gate
2 input NAND gate
A
B
C
(A.B.C)'

## Slide 11: The NOR Gate
NOR
Negative-AND

Outputs a 1 if all inputs are 0, and outputs a 1 otherwise.
3 input NAND gate

A
B
(A+B)'
A
B
(A+B)'
A
B
C
(A+B)'

## Slide 12: The XOR Gate
A
B
A  B
Outputs a 1 if the total number of ones in the inputs are odd.
For a 2-input XOR, it outputs a 1 when the two inputs are different
Can be extended to any number of inputs
2 input XOR
3 input XOR
A
B
C
A  B

## Slide 13: The XNOR Gate
A
B
(A  B)'
Outputs a 1 if the total number of ones in the inputs are even.
For a 2-input XNOR, it outputs a 1 when the two inputs, X and Y are the same
2 input XNOR
3 input XNOR
A
B
C
(A  B  B)'

## Slide 14: REPRESENTING DIGITAL LOGIC CIRCUIT USING BOOLEAN FUNCTIONS

## Slide 15: Representing a Boolean Function
We can use the logic gates to implement a Boolean function
A Boolean function is a function which takes Boolean variables (0 or 1) as input and generates a Boolean output value
Logic circuits of this type are called combinational logic circuits, since the variables are “combined” by using the various logical operations.
There are different two ways to represent a Boolean Function:
  Truth Table
  Boolean Expressions

## Slide 16: Truth Table
Provides a listing of every possible combination of inputs and its corresponding outputs.
Truth table can have different number of inputs or outputs. Example:
The input contains all permutations or possible combinations of input pattern.
They are the same for all circuits for the same number of input bits.
The output(s) reflect the way the circuit behaves.
It is different for different type of tasks

## Slide 17: Truth Tables
Create the truth table that generates an even-parity bit for a 3 bit input
Write the truth table to compute the square of a binary number, X1X0, and store the output in binary using 4 bits, Y3Y2Y1Y0.
Examples:

## Slide 18: Boolean Expression
Truth tables are useful in circuit analysis. Every function computed by a circuit can be specified by a truth table.
Truth tables are useful in circuit design. A truth table specifies the function to be computed precisely. Each truth table specifies a unique function.
Unfortunately, truth tables can be very cumbersome.
  When there are n inputs, a truth table contains 2n rows
  Cannot be manipulated to generate a cost-effective logic circuit especially for complicated circuits
  Only suitable for simple Boolean functions
Solution: Boolean Expression
  A Boolean expression is an algebraic statement containing Boolean variables and operators.

## Slide 19: Boolean Expression
A Boolean expression can be used to specify a Boolean function, which expresses the logical relationship between binary variables.
F = X + (Y.Z)
Truth Table
Boolean Expression

## Slide 20: Boolean Expression
A Boolean expression is a sequence of binary variables and logical operators.
A binary variable is a variable that has only two possible values, 0 or 1.
A logical operator is a symbol representing a logic gate:
  or X’ represents NOT X
  X ·Y or XY represents X AND Y
  X + Y represents X OR Y
  X  Y represents X XOR Y
  The expression (X+Y)’ represents X NOR Y
  The expression (X.Y)’ represents X NAND Y

## Slide 21: From Boolean Expression to Logic Circuit
When a boolean expression is provided, we can easily draw the logic circuit.
The precedence of gate operators are
  ()
  NOT
  AND, NAND
  OR, NOR, XOR
Wiring or interconnections:
Interconnected Not interconnected
Given a Boolean Expression, we can start draw the logic circuit from the output back to the inputs or the other way round.
a
a
a
a
a
b
a
b

## Slide 22: From Boolean Expression to Logic Circuit
(ii) F2 = x + y’ . z
(i) F1 = y’ + x . y’ . z
x.y’.z
y’
Step 1
y’x
z
Step 2
y
x
z
Step 3 (optional)
F1
2 input OR
3 input AND
2 input OR
2 input AND
INV
INV
INV
x
F2
y'.z
Step 1
x
y'
z
F2
Step 2
Step 3 (optional)
x
z
F2
y

## Slide 23: From Boolean Expression to Logic Circuit
(iii) F3 = x . y' + x’ . z
x'
z
F3
x'.z
x.y'
x
y'
Review Question:
Implement the logic circuit for the following Boolean circuits:
a) F = a . b . c + c . (d + e)’
b) F = (a + b.c).(b’ + d)
c) F = (x  y)’.z

## Slide 24: From Logic Circuit to Boolean Expression
b'.c'
a
b
c
e
Out
a+b'.c'
e.(a+b'.c‘)
e.b’.c’
e.b’.c’ + e.(a+b'.c‘)
1
2
3
4
A'.B'
A'.B'+C
(A'.B'+C)'
A'
B'
C
Out
1
2
3
When a logic circuit is provided, we can also analyse the circuit to obtain the logic expression.
Starting from the input, derive the Boolean Expression at each nodes. Derive the equations level by level until you reach the output(s).
Example 1:
Example 2:

## Slide 25: Contention in Circuit
Contention happens when two sources (or outputs) are connected together where the two sources has a different state (one with a value of 1 and another with a value of 0).
Causes high current in the circuit when the outputs are different and should be avoided.
1
1
1
1
1
0
0
0
1
0
1
1
X
1
0
Contention when the outputs generated by the two AND gates are conflicting
No problem when the outputs of both AND gates are the same

## Slide 26: Proof using Truth Table
We can use truth table to prove by perfect induction.
Prove that: x . (y + z) = (x . y) + (x . z)
Construct truth table for LHS & RHS of above equality.
(ii) Check that LHS = RHS
Postulate is SATISFIED because output column 2 & 5 (for LHS & RHS expressions) are equal for all cases.

## Slide 27: Proof using Truth Table
Example: Prove that
x + x’ . z = x + z

## Slide 28: TRUTHTABLE  BOOLEAN EXPRESSION  DIGITAL CIRCUIT

## Slide 29: Truth Table to Boolean Expression
Given only a truth table, how do we convert it to Boolean Expression?
This can be done by converting the truth table into a particular canonical form (a unique form for representing something).
There are two canonical forms of representing the Boolean Function of a truth table:
  Sum of Minterms
  Product of Maxterms
F = X + Y.Z

## Slide 30: Standard Terms of Boolean Expression
A literal is a Boolean variable or its negation.
  e.g. both X and X’ are literals.
A product term is the conjunction of several literals, i.e., the logical product of a number of literals.
  e.g. X.Y is a product term.
A sum term is the disjunction of several literals, i.e., the logical sum of a number of literals.
  e.g. Y + Z is a sum term.
Sum-of-Products (SOP) Expression: a product term or a logical sum (OR) of several product terms.
Examples: x
x.y‘ + x'.y.z A + B'.C + A.C‘ + C.D
Product-of-Sums (POS) Expression: a sum term or a logical product (AND) of several sum terms.
Examples: x
(x+y').(x'+y+z)
(A+B).(A'+B')

## Slide 31: Minterm
A minterm for a set of variables is a product term containing ALL the variables (or its inverted version) exactly once.
    For example, for a digital circuit with input variables X, Y and Z,
    X’.Y.Z is a minterm  contains the product term of all variables
    X’.Y is a product term but NOT a minterm  Z is not in the product term
There are 2n distinct minterms for n variables
  There are a total 4 minterms for a 2 input variable:
  Input variable = X and Y
  Minterms = X’.Y’, X’.Y, X.Y’, X.Y
  There are a total of 8 minterms for a 3 input variable
  Input variable = A, B an C
  Minterms = A’.B’.C’, A’.B’.C, A’.B.C’, A’.B.C
  A.B’.C’, A.B’.C, A.B.C’, A.B.C

## Slide 32: Minterm
For each input bit pattern in the truthtable, there is only one minterm which generates a 1 for that bit pattern
For the input X=1, Y=1, Z = 0, only the minterm X . Y . Z’ outputs 1.
All other minterms output 0.
For the input X=0, Y=0, Z = 0, only the the minterm X’ . Y’ . Z’ outputs 1.
All other minterms output 0.

## Slide 33: Minterm
From the previous observation, each minterm can be used to represent a particular bit pattern (row) in the truth table if it outputs a ONE (1).
This is because only the corresponding row will output 1 for that minterm. All other combinations will generate a 0. For example, for X=0, Y=1, Z=1, only the minterm X’.Y.Z will output 1.
X
Y
Z
X’YZ
In general, to form a minterm for a particular bit pattern variable, bits with a value of 0 will be complemented whereas bits with a value of 1 will NOT be complemented.
For example, the minterm for the input bit pattern 011 of the truth table is X’.Y.Z
Truth table for minterm X’.Y.Z

## Slide 34: Truthtable as a Combination of Minterm
  A truth table can be expressed in terms of the sum of minterm by looking at rows which outputs 1.
  Write down all the min-terms for rows with a value of 1 and OR them.
  F = 1 when either the bit pattern is 011 (covered by minterm X’.Y.Z) OR when the bit pattern is 110 (covered by minterm X.Y.Z’)
  F = X’ . Y . Z + X . Y . Z’
  OR

## Slide 35: Sum of MinTerms
Example: Express the following truthtable in terms of a Boolean Expression
F1 = x.y.z'
F2 = x'.y'.z + x.y'.z' + x.y'.z + x.y.z' + x.y.z
F3 = x'.y'.z + x'.y.z + x.y'.z' +x.y'.z
??
??
??

## Slide 36: Maxterm
A maxterm for a set of variables is a sum term containing ALL the variables (or its inverted version) exactly once.
    For example, for a digital circuit with input variables X, Y and Z,
    X’ + Y + Z is a maxterm  contains the sum term of all variables
    X’ + Y is a sum term but NOT a maxterm  Z is not in the sum term
There are 2n distinct maxterm for n variables
  There are a total 4 maxterm for a 2 input variable:
  Input variable = X and Y
  Minterms = X’ + Y’, X’. + Y, X + Y’, X + Y
  There are a total of 8 minterms for a 3 input variable
  Input variable = A, B and C
  Minterms = A’ + B’ + C’, A’ + B’ + C, A’ + B + C’, A’ + B + C
  A + B’ + C’, A + B’ + C, A + B + C’, A + B + C

## Slide 37: Maxterm
For the input X=0, Y=0, Z = 0, only the the minterm X’ . Y’ . Z’ outputs 1.
All other minterms output 0.
For each input bit pattern in the truthtable, there is
  only one minterm which generates a 1 for that bit pattern, and
  only one maxterm which generates a 0 for that bit pattern.
For the input X=0, Y=0, Z = 1, only the maxterm X + Y + Z’ outputs 0.
All other maxterms output 1
For the input X=1, Y=0, Z = 1, only the maxterm X’ + Y + Z’ outputs 1.
All other maxterms output 1.

## Slide 38: Truthtable as a Combination of Maxterm
  F = (X+Y’+Z’) . (X’+Y’+Z)
  A truth table can be expressed in terms of the product of maxterm by looking at rows which outputs 0.
  AND
  F = 1 only when the bit pattern is NOT 011 and NOT 110.
  F = 0 only when the bit pattern is either 011 (covered by maxterm X+Y’+Z’) OR when the bit pattern is 110 (covered by minterm X’+Y’+Z’)

## Slide 39: Maxterm vs Minterm
F expressed as Sum of MinTerm:
F = X’.Y.Z’ + X’.Y.Z + X.Y’.Z + X.Y.Z’ + X.Y.Z
Minterms expresses F using rows having 1 as output
row 2, X=0 Y=1 Z=0, minterm = X’.Y.Z’
row 3, X=0 Y=1 Z=1, minterm = X’.Y.Z
row 5, X=1 Y=0 Z=1, minterm = X.Y’.Z
row 6, X=1 Y=1 Z=0, minterm = X.Y.Z’
row 7, X=1 Y=1 Z=1, minterm =X.Y.Z
Literal is complimented when variable is 0
F expressed as Product of MaxTerm:
F = (X+Y+Z).(X+Y+Z’).(X’+Y+Z)
Maxterm expresses F using terms with 0 as output
row 0, X=0 Y=0 Z=0, maxterm = X + Y + Z
row 1, X=0 Y=0 Z=1, maxterm = X + Y + Z’
row 2, X=1 Y=0 Z=0, maxterm = X’ + Y + Z
Literal is complemented when variable is 1

## Slide 40: Review Question
F1 = (x+y+z).(x+y'+z).(x+y'+z')
F2 = (x+y+z).(x+y'+z).(x'+y'+z).(x'+y'+z')
Express the following truth table in terms of Product of Maxterms:

## Slide 41: Review Question
Exercise: Write the boolean expression for a circuit that perform the square of a 2-bit input. Express your answer both in terms of Product of Maxterms and Sum of Minterms.
Sum of Minterms:
Y0 = X1’.X0 + X1.X0
Y1 = 0
Y2 = X1.X0’
Y3 = X1.X0
Product of Maxterms:
Y0 = (X1 + X0).(X1’ + X0)
Y1 = (X1 + X0).(X1 + X0’).(X1’ + X0).(X1’ + X0’)
Y2 = (X1 + X0).(X1 + X0’).(X1’ + X0’)
Y3 = (X1 + X0).(X1 + X0’).(X1’ + X0)

## Slide 42: Two-level Circuit Design
A "standard form" of circuits. Every Boolean function described by a truth table can be converted into a Boolean expression in SOP or POS form.
To construct a circuit that computes a desired function,
  Step 1: Write down the truth table.
  Step 2: Convert the truth table into equivalent Boolean expressions in Sum of Minterm or Product of Maxterm
  Step 3: Simplify the logic circuit using Boolean Algebra.
  Step 4: Convert the Boolean expressions into an equivalent circuit diagram.

## Slide 43: Two-level Circuit Design
A SOP can be implemented by a 2-level circuit in which there are a number of AND gates in the first level and one OR gate in the second level. (We do not count the NOT gates and assume the AND, OR gates have enough fan-in.)
Example: . Then a 2-level circuit for F is:
Repeat this problem using the POS expression

## Slide 44: DIGITAL CIRCUIT SIMPLIFICATION USING BOOLEAN ALGEBRA

## Slide 45: Circuit Design
Representation of a function in Boolean expression is not unique, e.g. a function can be represented in either a POS or a SOP:
A Boolean expression does not completely dictate a circuit. Given a Boolean expression, one may construct different circuit diagrams. Some are better than the others. What is the “best” circuit?
  One with the fewest hardware.
  One with the fastest speed.
Finding the Best Design
Are these two equivalent?

## Slide 46: Circuit Design
The amount of hardware can be measured by the number of gates in the circuit.
Each gate takes a small (but non-zero) amount of time.
The speed of a circuit can be measured by the maximum no. of gates in a path (critical path) from an input to an output.
Two optimization methods:
  Boolean Algebra
  K-Map
Finding the Best Design

## Slide 47: Circuit Design
  Example: A + C(B + DE) = A + BC + CDE
  There is a tradeoff between size and speed. Optimizing one may sacrifice the other.
Finding the Best Design

## Slide 48: Boolean Algebra
Circuits are difficult to manipulate. Boolean expressions are easier to manipulate. We can simplify Boolean expressions using identities in Boolean algebra.
Boolean Algebra named after George Boole who used it to study human logical reasoning – calculus of proposition. Example: Either “it has rained” OR “someone splashed water”, The candidate “must be tall” AND “have good vision”.
Events: true or false
Connectives : a OR b; a AND b, NOT a
Resembles the algebra of real numbers but multiplication x.y is replaced with the AND operation, addition x + y is replaced with the OR operation and negation –x is replaced with the NOT operation.
What is an Algebra?
  set of elements (e.g. 0,1,2,..)
  set of operations (+ - * / ..)
  postulates/axioms (e.g. 0 + x = x,..)
What is an Boolean Algebra?
  set of two elements (0, 1)
  set of operations (+ . ’  )
  postulates/axioms (e.g. 0 + 1 = 1,..)

## Slide 49: Boolean Algebra Axioms
A Boolean algebra consists of a set of elements B ={0,1}, with two binary operations {+} and {.} and a unary operation {'}, such that the following axioms hold:
Identities (0 and 1)
  0 + x = x + 0 = x
  1 . x = x . 1 = x
Distributive laws:
  x . (y + z) = (x . y) + (x . z)
  x + (y . z) = (x + y) . (x + z)
Complement:
  x + x' = 1
  x . x' = 0
Closure: For every x, y in B,
  x + y is in B
  x . y is in B
Commutative laws:
  x + y = y + x
  x . y = y . x
Associative laws:
  (x + y) + z = x + (y + z)
  = x + y + z
  (x . y) . z = x .( y . z)
  = x . y . z

## Slide 50: Precedence of Operators
To lessen the brackets used in writing Boolean expressions, operator precedence can be used.
Precedence (highest to lowest): ' . +
Examples:
a . b + c = (a . b) + c
b' + c = (b') + c
a + b' . c = a + ((b') . c)
Use brackets to overwrite precedence.
Examples:
a . (b + c)
(a + b)' . c

## Slide 51: Boolean Albegra Theorem
1. Idempotency
x + x = x
x . x = x
2. Null
x + 1 = 1
x . 0 = 0
3. Involution.
(x')' = x
4. Absorption (1)
x + x.y = x
x.(x + y) = x
5. Absorption (2)
x + x'.y = x+y
x.(x' + y) = x.y
6. DeMorgan
(x + y)' = x'.y’
(x.y)' = x' + y‘
7. Consensus
x.y + x'.z = x.y + x'.z + y.z
  (x+y).(x'+z) = (x + y).(x’ + z).(y + z)
Apart from the axioms/postulates, there are other useful theorems.

## Slide 52: Boolean Algebra Theorem
  [For your information] More about the Consensus theorem:
x.y + x'.z = x.y + x'.z + y.z
  1st and 2nd term are mutually exclusive for output 1
  Basically y.z is redundant
    If y OR z = 0, y.z = 0 and has no impact towards the original equation.
    If both y AND z = 1, then either the first (x.y) or second term (x’.z) = 1
  The consensus of X.Y and X’.Z is Y.Z where Y.Z is known as the consensus term
(x+y).(x'+z) = (x + y).(x' + z).(y + z)
  1st and 2nd term are mutually exclusive for output 0
  Basically y+ z is redundant
    If y = 1 OR z = 1, y + z = 1 and has no impact towards the original equation
    If both y = 0 AND z = 0, either the fist term (x + y) or (x’+ z)= 0
  The consensus of (x + y) and (x’ + z) is (y+z) which is known as the consensus term

## Slide 53: Proving Boolean Equations
Theorems can be proved using the truth table method. (Exercise: Prove De-Morgan’s theorem using the truth table.)
They can also be proved by algebraic manipulation using axioms/postulates or other basic theorems.
Example: Prove the Theorem 4 (Absorption)
(a) x + x.y = x (b) x.(x + y) = x
x + x.y = x.(1 + y) (distributive)
= x.1 (complement)
= x (identity)
x.(x + y) = x.x + x.y (distributive)
= x + x.y (idempotency)
= x (Absorption 1)

## Slide 54: Boolean Algebra Theorems (Proof)
Example: Prove the Theorem 1 (Idempotency)
(a) x + x = x (b) x . x = x
x + x = (x + x).1 (identity)
    = (x + x).(x + x') (complement)
    = x + x.x' (distributive)
    = x + 0 (complement)
    = x (identity)
x.x = x.x + 0 (identity)
    = x.x + x.x’ (complement)
    = x.(x + x’) (distributive)
    = x.1 (complement)
    = x (identity)

## Slide 55: Boolean Algebra Theorems (Proof)
Example: Prove the Theorem 5 (Absorption)
(a) x + x'.y = x+y (b) x.(x' + y) = x.y
x + x’.y = (x + x’).(x + y) (Distributive)
    = 1.(x + y) (Complement)
    = x + y (Identity)
x . (x’ + y) = x.x’ + x.y (Distributive)
= 0 + x.y (Complement)
    = x.y (Identity)

## Slide 56: Boolean Algebra Theorems (Proof)
Exercise: Prove Theorem 7 Consensus
x.y + x'.z + y.z = x.y + x'.z
= x.y + x’.z + y.z.1 (identity)
= x.y + x’.z + y.z.(x+x’) (complement)
= x.y + x’.z + x.y.z + x’.y.z (distributive)
= x.y + x.y.z +x’.z + x’.y.z (commutative)
= x.y (1+ z) + x’.z(1 + y) (distributive)
= x.y.1 + x’.z.1 (null)
= x.y + x’.z (identity)

## Slide 57: Boolean Expression to Truth Table
Given a Boolean Expression, convert the expression into a truth table.
Example: F = a.b + a’.c + a’.b’.c’
F = 1 when a = 1 and b = 1, c = X
F = 1 when a = 0 and c = 1, b = X
F = 1 when a = 0 and b = 0, b = 0

## Slide 58: Boolean Expression to Truth Table
Generate the truth table for the following equation
Example: F = a.(b + c)’ + b’.c’
F = 1 when b = 0 and c = 0
F = 1 only when
a=1 AND (b + c)’ = 1
(b + c)’ = 1 only when b + c = 0
b + c = 0 when b=0 AND c = 0
 F = 1 when a=1 and (b=0 and c=0)

## Slide 59: Boolean Algebra for Circuit Simplification
A simpler Boolean expression often gives rise to a better circuit, though not always the best.
It will be assumed that the simplest algebraic expression is one with
  minimum number of terms and
  fewest number of literals in each term

## Slide 60: Boolean Algebra for Circuit Simplification
Example 1 Given the following truth table, generate a simplified circuit diagram
x1
x2
x3
f1
0
0
0
1
0
0
1
1
0
1
0
0
0
1
1
1
1
0
0
0
1
0
1
0
1
1
0
0
1
1
1
1
Answer:

## Slide 61: Boolean Algebra for Circuit Simplification
Example 2

## Slide 62: Review Question
Simplify the following Boolean expression using Boolean algebra:
= A.B + B.C.B + B.C.C
= A.B + B.C + B.C
= A.B + B.C
= (x + y.y’).(x’ + z)
= x.(x’ + z)
= x.x’ + x.z
= x.z
F = A.B + B.C.(B + C)
ans = A.B + B.C
F = (x+y).(x+y').(x'+z)
ans = x.z
F = x'.y.(z + y'.x) + y'.z
ans = z.x’ + z.y
= x’.y.z + x’.y’.x + y’.z
= x’.y.z + 0.y’ + y’.z
= y.x’.z + y’.z
= z.(x’.y + y)
= z.(x’+ y)
= z.x’ + z.y

## Slide 63: Review Question
Simplify the following Boolean expression using Boolean algebra:
F = a.b.c + a.b.d + a'.b.c' + c.d + b.d '
Ans: B + CD
= a.b.c + a.b.d + a'.b.c' + c.d + b.d'
= a.b.c + a.b + a'.b.c' + c.d + b.d' (absorption)
= a.b.c + a.b + b.c' + c.d + b.d' (absorption)
= a.b + b.c' + c.d + b.d' (absorption)
= a.b + c.d + b.(c' + d') (distributivity)
= a.b + c.d + b.(c.d)' (DeMorgan)
= a.b + c.d + b (absorption)
= b + c.d (absorption)
Number of literals reduced form 13 to 3.

## Slide 64: DIGITAL CIRCUIT SIMPLIFICATION USING K-MAP

## Slide 65: K-MAP for Circuit Simplification
Boolean expressions are very open-ended (to your desired form)
But yet it may not be easy to identify the variables to be grouped when the number of terms is large
  Requires good algebraic manipulation skills
  Circuit may be sub-optimal when grouping of terms is not optimal
For some digital circuits, some combination may be invalid / unused (i.e. Don’t care situations).
For example, In BCD circuit, 1010 (ten) up to 1111 (fifteen) are “Don’t care” combinations.
It is not quite possible to use just Boolean algebra to optimally simplify expressions with “Don’t care” combinations

## Slide 66: Constructing a K-Map
K-Map can be used to simplify Boolean expressions easily and visually. (Even if there are “Don’t care” combinations. K-Map is a re-draw of truth table:
For more than 1 variable, the order of the columns and rows must be based on the Gray Code (00,01,11,10), so that adjacent rows/columns differ by one single variable
K-Map with more than 4 variables is messy.
The order of the variables CD and AB
is a Gray Code sequence

## Slide 67: Constructing the K-Map
Example:
X\YZ | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
XY\Z | 0 | 1
00 | 0 | 1
01 | 1 | 0
11 | 0 | 1
10 | 0 | 1
Truth Table:
Valid K-MAPs:
These two kmap tables are equivalent
The grouping of variables in the rows or columns can be freely done as long as the order follows the gray code

## Slide 68: Grouping Adjacent Cells
All cells in an n-variable K-MAP has n neighbours. Two cells are neighbours if they are different by one variable only
The neighbours of a cell is the cell on its left/right and top/right.
For example, for a 4-variables KMAP, the neighbours of A’BC’D are A’B’C’D, A’BC’D’, ABC’D and A’BCD
For boundary cells, there is wrap-around in the K-map:
  Horizontally: A’BCD’ is adjacent to A’BC’D’
  Vertically: A’B’C’D’ is adjacent to AB’C’D’
AB\CD | 00 | 01 | 11 | 10
00 |  | N1 |  | 
01 | N2 | X | N3 | 
11 |  | N4 |  | 
10 |  |  |  | 
AB\CD | 00 | 01 | 11 | 10
00 | N1 |  |  | 
01 | X | N3 |  | N2
11 | N4 |  |  | 
10 |  |  |  | 
AB\CD | 00 | 01 | 11 | 10
00 | N4 |  |  | 
01 |  |  |  | 
11 | N1 |  |  | 
10 | X | N3 |  | N2

## Slide 69: Grouping Adjacent Cells
Circuit simplication using K-MAP is about grouping a rectangle block of neighbours. Each group of adjacent minterms corresponds to a possible product term of the given function.
There are two ways of grouping:
  Sum of Product (SOP):
  Group cells with value of ones
  Product of Sum (POS):
  Group cells with value of the zeros
Rules for grouping cells:
  Different groups may overlap each other.
  A group must be rectangle in shape (also valid for wrap-around border cell)
  The rows and columns of a group must be in the power of twos (1,2,4,8,16,…) in size.
  Valid configurations of the group are like 1x1, 1x2, 2x2, 4x1, 4x4, 8x1, …
Grouping for SOP
Grouping for POS
1
1
00
01
11
10
00 01 11 10
wx
yz
1
1
1
1
1
1
0
0
00
01
11
10
00 01 11 10
wx
yz
0
0
0
0
0
0

## Slide 70: Grouping Adjacent Cells
Grouping for SOP
Grouping for SOPOSP
1
1
00
01
11
10
00 01 11 10
wx
yz
1
1
1
1
1
1
0
0
00
01
11
10
00 01 11 10
wx
yz
0
0
0
0
0
0
To simplify using K-MAP, the objective is find the blocks that covers all the 1s for SOP (or 0s for POS) such that
All blocks are valid blocks
There are as few group as possible: The fewer group, the less number of term.
  The blocks are as huge as possible: The larger a group, the fewer the number of literal in the term.

## Slide 71: K-MAP for SOP
How does grouping adjacent cells simplify a Boolean Expression?
In a K-map, each cell containing a ‘1’ corresponds to a minterm of a given function F.
Based on the Complement Theorem:
A + A' = 1
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 1 | 1 | 1
Grouping two adjacent column cells essentially eliminates one literal (the literal that changes between two neighbouring cell). The same applies to row cells. For example
A’.B.C’.D + A’.B.C.D = A’.B(C’+C).D = A’.B.D
Grouping four adjacent column cells essentially eliminates two literal . The same applies to the row cells. For example
A.B’.C’.D’ + A.B’.C’.D + A.B’.C.D’+ A.B’.C.D = A.B’.C’ + A.B’.C’ + A.B’.C + A.B’.C
= A.B’

## Slide 72: K-MAP for SOP
  Grouping of n cells will eliminate log2n literals:
    Grouping 1 cell eliminates 0 literal
    Grouping 2 cells eliminates 1 literal
    Grouping 4 cells eliminates 2 literals
    Grouping 8 cells eliminates 3 literals
    Grouping 16 cells eliminates 4 literals
  The terms with opposing literals (both un-negated and negated literals) will be kicked out.
  Steps to express the product term for a group in SOP:
    1) Get the literals for the row and column separately.
    2) Get the product of all the literals
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0
A’.B.D
Column-wise:
  2 columns  1 literal kicked out  C contains opposing literal and will be kicked out  remaining D
Row-wise:
  1 row  0 literal kicked out  remaining A’ as well as B
Group literal into a product term: A’.B.D
A’
B
D

## Slide 73: K-MAP for SOP
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 1 | 0 | 0 | 0
11 | 1 | 0 | 0 | 0
10 | 1 | 0 | 0 | 0
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 1
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 1 | 0 | 0 | 1
Four rows  A and B is kicked off
One column only  C’.D’
C’.D’
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 1
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0
A’.B’
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 1 | 0
11 | 0 | 1 | 1 | 0
10 | 0 | 0 | 0 | 0
B.D
Row: A is kicked off
Column: C is kicked off
B’.D’
  Grouping 4 cells will eliminates 2 literals

## Slide 74: K-MAP for SOP
  Grouping 8 cells eliminates 3 literals
AB\CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 1 | 1
01 | 1 | 1 | 1 | 1
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0
A’
  In general, grouping 2n squares eliminates n variables.
Invalid groups are groups which are
  Non- rectangular, or
  The row or column size is not in the power of 2
1
1
1
1
1
1
1
1
1
1
×
1
1
1
1
1
1
×
×
×

## Slide 75: K-MAP for SOP
P
O
P
K-Map summarization method
1) Get an optimal groups for the K-Map
  Start by constructing with the largest groups. For instance, look for the possibilities to group 8 cells, followed by 4, 2 and then 1 cells.
  If there are different groups for the same size, select the groups that will provide the maximum coverage (covers the most number of 1s with the minimum number of groups)
  Proceed until all 1s have been covered
  Get the product terms for all groups
  Sum the product terms to get the final simplified Boolean Expression
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
O
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 76: K-MAP for SOP
Example: Simplify Z = A’B’C’ + A’B + ABC’ + AC using the K-MAP
A\BC | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1
(2) A’B’
(1) C
(3) AB
F = A’B’ + AB + C

## Slide 77: K-MAP for POS
Simplified POS expression is similar to its SOP counterpart with the following differences:
  Instead of grouping ‘1s’, we now group ‘0s’.
  Each term is now a sum term (X+Y+Z) instead of product term (X.Y.Z)
  Each literal in the sum term needs to be complemented if its value is 1.
  For example: (Column 01)  A’.B for SOP
  (Column 01) A + B’ for POS
  The final term for POS is a product of all the sum terms (S1.S2.S3) instead of a sum of product terms (e.g. P1 + P2 + P3)

## Slide 78: K-MAP for POS
00
01
11
10
1
1
00 01 11 10
CD
AB
1
0
1
1
1
1
1
1
1
0
0
0
0
0
B’+D
A’+B’
To ensure F = 1, the input
must not fall into this
column (this is true when
either A = 0 or B = 0)
F = (A’+B’).(B’+D)
Example:

## Slide 79: K-MAP with Don’t Care States
In certain problems, some outputs are not specified.
These outputs can be either ‘1’ or ‘0’.
They are called don’t-care conditions, denoted by X (or sometimes, d).
Example: An odd parity generator for BCD code which has 6 unused combinations.

## Slide 80: K-MAP with Don’t Care States
Don’t-care conditions can be used to help simplify Boolean expression further in K-maps.
They could be chosen to be either ‘1’ or ‘0’, depending on which gives the simpler expression.
For comparison, the odd parity generator generated with and without Don’t Care states:
1
00
01
11
10
00 01 11 10
AB
CD
1
1
1
1
X
X
X
X
X
X
1
00
01
11
10
00 01 11 10
AB
CD
1
1
1
1
  WITH don’t-cares:
P = A'.B'.C'.D' + B'.C.D + B.C'.D
+ B.C.D' + A.D
  WITHOUT don’t-cares:
P = A'.B'.C'.D’ + A'.B'.C.D + A'.B.C'.D
+ A'.B.C.D' + A.B'.C'.D

## Slide 81: Example
B.D
A'.B.C'
A.B'.D'
1
1
C
A
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
D
1
1
1
A'.B'.C
f(A,B,C,D) = B.D + A'.B.C' + A.B'.D' + A'.B'.C
1
1
00
01
11
10
00 01 11 10
B
CD
AB
1
1
1
1
1
1
1

## Slide 82: Review Questions
1
1
00
01
11
10
00 01 11 10
CD
AB
1
1
1
1
1
1
1
1
X
00 01 11 10
CD
AB
X
1
X
1
1
X
00
01
11
10
Ans: F = AC + AD + B’D’
Ans: F = A’B’ + B’D’ + BCD