## Slide 1
UECS1013 Introduction to Computer Organisation and Architecture
Lecture 5:
Computer Architecture &
Assembly Language
(ARM Processor)

## Slide 2: Complex Instruction Set Computing (CISC)
An architecture with complex instruction set which combines multiple operations within a single instruction. Shifts the burden to the processor (hardware) which has to implement complicated instructions.
Extensive instruction set. E.g. multi-clock complex instructions,
  register-memory transfer + ALU operations
  memory-to-memory data transfer: Move the content from memory location A to the memory location B
MOVE A, B
“LOAD” and “STORE” incorporated within this single instruction
Most common microprocessors are based on CISC:
  Motorola 68000 family
  Intel x86 architecture based processors.
  System/360(excluding the 'scientific' Model 44), VAX, PDP-11, etc.

## Slide 3: Complex Instruction Set Computing (CISC)
Pros:
Simple and smaller codes. Less instructions are needed per-program. This reduces the frequency of accessing the slow main memory.
Smaller codes  consumes less memory  Save money (expensive during those days)
Only requires a simple compiler since the micro program has taken care of the intermediate operations

## Slide 4: Complex Instruction Set Computing (CISC)
Cons:
Many instructions are too specialized and infrequently used – only 20% of the instructions are used in a typical program.
Hardware tends to become more complex. Multiple operations lead to many different kinds of instructions that access memory.
The complexity of instructions varies significantly
   Different instruction length (instruction alignment consideration)
   Execution time for fetch-decode varies (timing issues)
CISC machines tend to become more complex for newer generations which are typically the superset of the older generations.
Commands needs to be translated into a series of microcode commands for execution  Tends to run slower than an equivalent series of simpler commands in RISC (do not require microcode translation).

## Slide 5: Reduced Instruction Set Computing (RISC)
Emerged around early 1980s with IBM 801, Stanford MIPS and UC-Berkeley RISC 1 and 2.
Designers found that existing processor ISAs had extensive instructions that were too complex.
Design philosophy: use the minimum set of instruction set to carry out all essential operations
  Once cycle execution time: RISC processors have a CPI of one cycle owing to a simple instruction set
  Pipelining: Allows the simultaneous execution of multiple instruction by breaking the instruction into multiple independent stages/parts.
  Large number of registers: The savings in complexity for a smaller instruction set translates to a larger number of registers. This helps to minimize the overhead caused by passing parameters on the stack (in the memory) by directing the subroutine to use a subset of registers

## Slide 6: Reduced Instruction Set Computing (RISC)
Consistency among instructions is achieved by
  Using few simple instructions that are of the same length
  Memory access is achieved only through explicit data movement commands such as the load and store instructions
  Each instruction performs less work but instruction execution time among different instructions is consistent
The complexity of the operations is moved from ISA to the domain of the assembly programmer/compiler  RISC requires more powerful compiler compared to CISC to translate high-level languages to machine languages
The codes in RISC are longer than CISC but they run faster.
Example RISC Processors:
Apple iPods (custom ARM7TDMI SoC) Apple iPhone (Samsung ARM1176JZF), Palm and PocketPC PDAs and smartphones (Intel XScale family, Samsung SC32442 - ARM9), Nintendo Game Boy Advance (ARM7), Nintendo DS (ARM7, ARM9), Sony Network Walkman (Sony in-house ARM based chip), Some Nokia and Sony Ericsson mobile phones

## Slide 7: CISC versus RISC
CISC
Speed up by reducing #instructions per program
Example:
MULT 2:3, 5:2
Emphasis on hardware
Memory-to-memory operations are allowed
Transistors used for implementing a huge set of complex instructions
Multi-clock, non-standardized length instruction
RISC
Speed up by shortening average #cycle/instruction and seconds/cycle
Example:
  LOAD A, 2:3, LOAD B, 5:2,
  PROD A, B, STORE 2:3, A
Emphasis on software
Register to register where LOAD and STORE are independent instructions
Less transistors for core, resulting in larger register and cache size.
Single-clock and common-length instructions

## Slide 8: Hybrid Processors
Recent advances in compiler technology, compiler capability and memory speed and fabrication technology blurs the line between RISC and CISC
Most modern microprocessor is a hybrid.
  Modern RISC supports chips as much instructions as yesterday’s CISC chips.
  Many CISC chips use many techniques which are previously only limited to RISC such as pipelining.
  CISC and RISC systems are becoming more and more alike.

## Slide 9: ARM Processor
ARM: “Advanced RISC Machine”
IP Core Provider:
  Does not manufacture its own VLSI devices
  Sells license to use its core design to electronic companies such as Apple, Samsung, Philips, ATMEL, Sharp, ST and TI.
ARM is one of the most widespread processor cores in the world
  In 2007, 98% of new cell phones uses ARM processor and as of 2009, 90% of all embedded 32-bit processors was an ARM. Recently, Cortex-A is used in IPAD.
Why ARM?
  Low power, low cost, tiny: Suitable for portable devices
  Good performance

## Slide 10: ARM Processor
ARM7 uses von Neuman Architecture (single bus for both data and instruction) while ARM9 and Cortex uses the Harvard Architecture (separate data and instruction bus).
We will be concentrating on ARM 7

## Slide 11: ARM Processor
All instructions are 32 bits long.
Most instructions execute in a single cycle.
Every instruction can be conditionally executed.
RISC-based (load/store) architecture
  Data processing instructions act only on registers
  LDR and STR instructions for memory and register data transfer
  Combined ALU and shifter for high speed bit manipulation
  Specific memory access instructions with powerful auto-indexing addressing modes.
    Flexible multiple register load and store instructions

## Slide 12: ARM Processor
Registers: High-Speed
(local) memory
Arithmetic & Logical Unit
Control
unit
Interface to bus and external devices

## Slide 13: Register Organization
ARM has 37 registers in total, all of which are 32-bits long.
  30 general purpose registers
  1 dedicated program counter (PC)
  1 dedicated current program status register (CPSR)
  5 dedicated saved program status registers (SPSR)

## Slide 14: Status Registers (CPSR and SPSR)
Holds information of the most recently executed ALU operation if suffix “S” is attached to the instruction.
Control the enabling and disabling of interrupts.
Set the processor operating mode
Copies of the ALU status flags (latched if the
instruction has the "S" bit set).
N = Negative result from ALU flag.
Z = Zero result from ALU flag.
C = ALU operation Carried out
V = ALU operation oVerflowed
* Interrupt Disable bits.
I = 1, disables the IRQ.
F = 1, disables the FIQ.
* T Bit (Architecture v4T only)
T = 0, Processor in ARM state
T = 1, Processor in Thumb state
* Condition Code Flags
Mode
N
Z
C
V
28
31
8
4
0
I F T
* Mode Bits
[4:0] define the processor mode.
Notes: Similarly in other 4 modes, though here only r13->r14 swapped.
“Banked” registers stored between mode swaps. Useful for interrupt handling because nothing to set up. Can thus run more quickly.

## Slide 15: Status Registers (CPSR and SPSR)
N (Negative Flag)
  Indicates a negative in the arithmetic operation
  Example (Subtract 10 from R2)
  SUBS R6, R2, R3 ; R2 = 2, R3 = 10
  (CPSR will be updated, N = 1)
  SUB R6, R2, R3 ; R2 = 2, R3 = 10
  (CPSR will NOT be updated, N is not updated)
Mode
N
Z
C
V
28
31
8
4
0
I F T

## Slide 16: Status Registers (CPSR and SPSR)
Z(Zero Flag)
  Indicates a zero in the arithmetic operation
  Example (Subtract 10 from R2)
  SUBS R6, R2, #10 where R2 = 10
C(Carry Flag)
  Operations (e.g. addition) results in carry
  Example:
  ADDS R6, R2, #0xFFFFFFFF where R2 = #0xFFFFFFFF = -1
  Does not necessarily cause overflow. For example, addition of negative numbers may generate a carry but no overflow.
Mode
N
Z
C
V
28
31
8
4
0
I F T

## Slide 17: Status Registers (CPSR and SPSR)
V (Overflow Flag)
  An arithmetic overflow has occurred.
  Example: ADDS R6, R2, #0x7FFFFFFF where R2 = #0x7FFFFFFF
  Two positive number produces a negative number in 2nd Complement!
Mode
N
Z
C
V
28
31
8
4
0
I F T

## Slide 18: Program Counter
PC is used to point to the next instruction to be executed
All instructions are 32 bits in length and therefore all instructions must be word aligned
Therefore the PC value is stored in bits [31:2] with bits [1:0] equal to zero (as instruction cannot be halfword or byte aligned).
0x00004004
PC
Example: A + B
Currently executed instruction is at address 0x4000
LDR R2, B
LDR R1, A
ADD R1, R1, R2
0x4000
0x4004
0x4008
Memory

## Slide 19: Operating Modes
Although there are 37 registers in total, a programmer have access to maximum of 17 registers in user mode and 18 in privileged mode
The ARM has six different operating modes:
  User: unprivileged mode under which most tasks run
  Privileged Modes:
  IRQ: raised when an external device raises a normal interrupt request
  FIQ: entered when an external device raises a fast-interrupt request to obtain urgent service
  Supervisor: entered on reset and when a Software Interrupt instruction (SWI) command is executed by a user program
  Abort: used to handle memory access violations
  Undef: used to handle undefined instructions

## Slide 20: Operating Modes
General registers and Program Counter
Program Status Registers
r15 (pc)
r14 (lr)
r13 (sp)
r14_svc
r13_svc
r14_irq
r13_irq
r14_abt
r13_abt
r14_undef
r13_undef
User32/System
FIQ32
Supervisor32
Abort32
IRQ32
Undefined32
cpsr
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
cpsr
cpsr
cpsr
cpsr
cpsr
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
spsr_undef
spsr_irq
spsr_abt
spsr_sup
spsr_fiq

## Slide 21: Operating Modes
The register files are arranged into several banks. The set of registers which are accessible depends on the mode. Example:
  R0 to R6 can be accessed in all modes
  An assembly program running in user mode is allowed access to R8 but a program running in FIQ mode do not, but instead have access to a different register, R8_FIQ.
Each mode can access
  a particular set of R0-R12 registers.
  R15 (the program counter)
  CPSR (the current program status register)
  a particular r13 (the stack pointer) and r14 (link register)
and privileged modes can also access
  a particular SPSR (saved program status register)

## Slide 22: Operating Modes
From User Mode to FIQ Mode
Notes: Similarly in other 4 modes, though here only r13->r14 swapped.
“Banked” registers stored between mode swaps. Useful for interrupt handling because nothing to set up. Can thus run more quickly.

## Slide 23: Assembly Language
  Why assembly language?
  Many system-level developer will continue to program in assembly language to have more control over the processor.
  Writing assembly language programs helps to understand computer architecture.
  Many application require the efficiency of assembly language
  Learning assembly language helps to know what is happening inside the computer.
  The foundation of many abstract concepts in high-level programming languages and operating systems etc. closely related to assembly language and computer architecture.

## Slide 24
Assembly Language
Common operations of the processors: Data Movement, Flow Control, Logical, Shift, I/O, etc.
Most programs spend over 70% of the time executing instructions from the Data Movement and Flow Control.
D.A. Patterson and D.R. Ditzel, “The case for the reduced instruction set computer”, Computer Architecture News, Vol 9(3), 1980.

## Slide 25
Assembly Language
Basic format:
  2 variables (destination + source)
  3 variables (destination + left source + right source)
  Use semi-colon to put comments at the end of statement. All good programs should have high quality comments
  Use label to mark current instruction, used in other parts of the program to refer to current instruction
Extended format:
Format of an ARM Instruction
MOV r4, r0 ; a comment r4  r0
Label ADD r4, r0, r1 ; a comment r4  r0+r1
destination
source/left
source/right
instruction
  ADD<cc><s> r4, r0, r1
Conditional execution
CPSR update

## Slide 26: Writing your first assembly code
Description:
Write a procedure which adds the content in memory location A and B. Store the result into memory location C.
[C] = [A] + [B]
Input: [A] = 0xA, [B]=0x14
Output: [C]
Write the assembly code to perform the following task:
Notes:
A, B and C are labels which specifies location of the memory (they are just the address in the memory).
[A] are the contents of the memory at the location A.

## Slide 27: The Assembly Process
Write the source program (.s) created using text editor. Using Keil uVision editor to create the source code provides the color code
Assembler
  Translates source file to object code (.o)
  Recognizes mnemonics for OP codes
  Interprets addressing modes for operands
  Recognizes directives that define constants and allocate space in memory for data
  Labels and names placed in symbol table (.map)
Write source program (.s)
Machine code
(.o)
Memory map file
(.map)
List file
(.lst)
Hardware Execution
Simulation
Keil uVision
Debugging
&
verification
assembler

## Slide 28: Structure of an Assembly Code
TTL Addition
AREA Program, CODE, READONLY ; start of code
ENTRY
Main
LDR R1, A ; Load content of A into R1
LDR R2, B ; Load content of B into R2
ADD R1, R1, R2 ; ADD and store in R1
STR R1, C ; Store the result
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE ; start of data
A DCD 0x0000 000A ; 10
B DCD 0x0000 0014 ; 20
C DCD 0 ; last data
END
Comments
Code
Data
End of Program
Title of Program

## Slide 29: Structure of an Assembly Code
TTL Addition
AREA Program, CODE, READONLY ; start of code
ENTRY
Main
LDR R1, A ; Load content of A into R1
LDR R2, B ; Load content of B into R2
ADD R1, R1, R2 ; ADD and store in R1
STR R1, C ; Store the result
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE ; start of data
A DCD 0x0000 000A ; 10
B DCD 0x0000 0014 ; 20
C DCD 0 ; last data
END
Opcodes/Directives
Operands
Code Labels
Data
Labels

## Slide 30: Skeleton of an assembly program
TTL MyProgram
Put your EQU statements here (e.g., N EQU 12)
AREA MyCode, CODE, READONLY ; start of code
ENTRY
Main
Write your program here (e.g. LDR R0, A)
HERE BAL HERE ; end of code
AREA MyData, DATA, READWRITE ; start of data
Define your data here (e.g., Width DCD 0x12)
; end of data
END

## Slide 31: Writing your first assembly code
The corresponding assembly program for the aforementioned problem:
TTL Addition
AREA Program, CODE, READONLY ; start of code
ENTRY
Main
LDR R1, A ; Load content of A into R1
LDR R2, B ; Load content of B into R2
ADD R1, R1, R2 ; Perform A + B
STR R1, C ; Store the result into C
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x0000000A ; start of data
B DCD 0x00000014
C DCD 0 ; end of data
END

## Slide 32: Good Programming Practice
Good Programming Practice
Use instructive names for your variables. Example
x, y, z v.s. width, length, area
Put comments (and good ones) to describe your program
Align your programs using tabs/space
Why is this important?
When your program gets bulky, a good programming practice will make your code more readable and manageable
Allows other engineers/programmer to understand your code easily
You can recall your program easily after you leave it for a period of time
A clean code is easy to debug

## Slide 33: Good Programming Practice
A badly written Program
…
LDR R1, A
LDR R2, B
ADD R1, R1, R2
STR R1, C
…
Area Data, DATA, READONLY
B DCD 2
A DCD 0x1
C DCD 0x2

## Slide 34: Good Programming Practice
A better program:
TTL Addition
AREA Program, CODE, READONLY ; start of code
ENTRY
Main
LDR R1, A ; Load content of A into R1
LDR R2, B ; Load content of B into R2
ADD R1, R1, R2 ; Perform A + B
STR R1, C ; Store the result into C
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x0000000A ; input data A
B DCD 0x00000014 ; input data B
C DCD 0 ; output data C
END
A good comment allows us to understand the program
The labels, opcode, operand and comments should be well separated. Use ‘TAB’ to align the columns

## Slide 35: Basic ARM Instructions
LDR <Register>,<Label>
Transfer data from memory location (pointed by label) to register
STR <Register>,<Label>
Transfer data from register to memory location (pointed by label)
DCD <val>
Define a word data in data region

## Slide 36: Example 1
Description:
Write a procedure which copies the value from memory location in A to B. Store
[B] = [A]
Input: [A]=0x2
Output: [B]
Write the assembly code to perform the following task:
0x2
Memory
A
B

## Slide 37: Example 1
TTL
AREA , CODE, READONLY
ENTRY
Main
LDR R1, A ; R1  [A]
STR R1, B ; [B]  R1
HERE BAL HERE ; end of code
AREA , DATA, READWRITE
A DCD 0x2 ; input (hexadecimal)
B DCD 0 ; output (initialize to 0)
END
CopyOneItem
MyFirstProgram
MyData

## Slide 38: Basic ARM Instructions
MUL <Rdest>, <Rsource1>,<Rsource2>
Rdest = Rsource 1 x Rsource2
ADD <Rdest>, <Rsource1>, <Rsource2>
Rdest = Rsource 1 + Rsource2
ADD <Rdest>, <Rsource1>, #<Value>
Rdest = Rsource 1 + Value
SUB <Rdest>, <Rsource1>, <Rsource2>
Rdest = Rsource 1 - Rsource2
SUB <Rdest>, <Rsource1>, #<Value>
Rdest = Rsource 1 - Value

## Slide 39: Example 2
Description:
Write a procedure which performs the following operation
y = x2 + 4
Input: [X] = 10
Output: [Y]
Write the assembly code to perform the following task:
0xA
Memory
X
Y

## Slide 40: Example 2
TTL Func1
AREA MyProgram, CODE, READONLY
ENTRY
Main
LDR R1, X ; R1  [X]
MUL R2, R1, R1 ; R2  X2
ADD R2, R2, #4 ; R2  X2 + 4
STR R2, Y ; [Y]  R2 (result)
HERE BAL HERE ; end of code
AREA MyData , DATA, READWRITE
X DCD 10 ; input (decimal)
Y DCD 0 ; output (initialize to 0)
END

## Slide 41: Basic ARM Instructions
MOV <Rdest>, #value
Update Rdest with value
MOV <Rdest>,<Rsource>
Transfer data from Rsource to Rdest
LDR <Rdest>, =<Label>
Load Rdest with the memory address that label represents (not the content pointed by label)
LDR <Rdest>, [<Rsource>]
Load Rdest with the memory address that pointed by Rsource
STR <Rsource>, [<Rdest>]
Store Rdest into the memory address pointed by Rdest

## Slide 42: Example 3:
Description:
Write a procedure which resets a three-item array in memory location A to 0.
Input: [A]=12, 13, 14
Output: [A] = 0, 0, 0
Write the assembly code to perform the following task:
12
13
Memory
A
14

## Slide 43: Example 3
TTL ResetArray
AREA Program, CODE, READONLY
ENTRY
Main
MOV R0, #0
LDR R1, =A ; R1 = A (first item in array A)
STR R0, [R1] ; Set [A] = 0
ADD R1, R1, #4 ; R1 = A + 4 (second item)
STR R0, [R1 ] ; Set [A + 4] = 0
ADD R1, R1, #4 ; R1 = A + 8 (third item)
STR R0, [R1] ; Set [A + 8] = 0
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 12, 13,14 ; array A (2 items)
B DCD 0, 0 ; array B (2 items)
END

## Slide 44: Example 4
Description:
Write a procedure which copies a two-items array from memory location in A to B.
[B] = [A]
[B+4] = [A+4]
Input: [A]=0x2, [A+4]=0x4
Output: [B], [B+4]
Write the assembly code to perform the following task:
0x2
0x4
Memory
A
B

## Slide 45: Example 4
TTL CopyTwoItems
AREA Program, CODE, READONLY ; start of code
ENTRY
Main
LDR R1, =A ; R1 = A (first item in array A)
LDR R2, =B ; R2 = B (first item in array B)
LDR R3, [R1] ; Get [A]
STR R3, [R2] ; [B]  [A]
ADD R1, R1, #4 ; R1 = A + 4 (second item in array A)
ADD R2, R2, #4 ; R2 = B + 4 (second item in array B)
LDR R3, [R1] ; Get [A+4]
STR R3, [R2] ; [B+4]  [A+4]
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x2, 0x4 ; array A (2 items)
B DCD 0, 0 ; array B (2 items)
END

## Slide 46: CONDITIONAL OPERATION

## Slide 47
Conditional Update of Status Register
instruction<s>
The processor execute the instructions pointed by Program Counter. It will additionally update the CPSR register if the instruction is appended with <s> :
  N (negative), Z (zero), C(carry), V(overflow)
Example:
MOVS R0, R1 ; will set the N and Z flags
; depending on the value of R1
MOV R0, R1 ; CPSR will NOT be updated
The CPSR is updated depending on the result of the operation. For example:
ADDS R1, R2, R3
if R2 = -1, R3 = 1, then NZCV = 0110 ; zero and carry set
if R2 = 10, R3 = -20, then NZCV = 1010 ; negative and carry set

## Slide 48
Almost all ARM instruction contain a condition field which allows it to be executed conditionally. Add the postfix <cc> to specify condition.
Examples:
ADDS R0, R1, R2 ; R0  R1 + R2, update CPSR
MOVEQ R5, R1 ; Conditional execution
  R5 is updated only if R0 (from previous addition) is equal to zero. Else the second instruction will not be executed.
MOVSEQ R5, R1 ; Conditional execution + update CPSR.
An instruction will be/will not be executed depending on
  The values of CPSR register which are updated by the a previously executed instruction (not necessarily the most recent one)
  The type of conditions that are specified by <cc>
Conditional Execution of Instructions
instruction<cc>

## Slide 49
The complete set of conditional flags <cc> that can be used
Conditional Execution of Instructions
instruction<cc>

## Slide 50
Greater (GT, GE) and Less (LT, LE) conditions are used for signed number
Higher (HI, HS) and Lower (LO, LS) conditions are used for unsigned number
Can also be used after the comparison (CMP) instruction.
Example 1:
Assume R1 = 0xFFFFFFFF and R2 = 0x00000001
CMP R2, R1 ; Is the signed value of R2 greater than R1?
BGT LOC ; YES (1>-1), branch to LOC
CMP R2, R1 ; Is the unsigned value of R2 greater than R1?
BHI LOC ; NO (1< 4294967295), do not branch
……
Example 2 Example3
Conditional Execution of Instructions
instruction<cc>

## Slide 51: SHIFTER OPERAND

## Slide 52
Shifter Operand
Instruction <Rd>,<Rs1>,<shifter_operand>
Instruction <Rd>, <shifter_operand>
Name | Shifter_Operand | Example
Immediate | #Value | MOV R0, #2
(2) Register Direct | Rs2 | MOV R0, R1
(3) Register Direct + Barrel Shifter |  | 
a) Logical Left-Shift (LSL) | Rs2, LSL <shift> | Add R1, R2, LSL #2
b) Logical Right-Shift (LSR) | Rs2, LSR <shift> | Add R1, R2, LSR #2
c) Arithmetic Right-Shift (ASR) | Rs2, ASR <shift> | Add R1, R2, ASR #2
d) Rotate Right (ROR) | Rs2, ROR <shift> | Add R1, R2, ROR #2
e) Rotate Right Extended (RRX) | Rs2, RRX<shift> | Add R1, R2, RRX #2

## Slide 53
Immediate
The simplest addressing mode is to take an immediate value, as the 2nd operand.
All ARM instructions are 32 bits long.
The operand is embedded within the instruction word and occupies 8 bit. This gives a range of 0 to 255 for immediate value.
Example:
MOV R0, #0xC
ADD R0, R1, #4 ; R0  R1 + 4
R0
0x0000 000C
Shifter Operand 1: Immediate
Instruction <Rd>,<Rs1>,<shifter_operand>
Instruction <Rd>,<shifter_operand>

## Slide 54
R0
0x0000 4000
R1
xxxx xxxx
Register Direct
The Register Direct addressing mode transfers data between registers
Example: Transfers register content from R0 to R1
  MOV R1, R0
  ADD R1, R2, R3 ; R1  R2 + R3
Shifter Operand 2: Register Direct
Instruction <Rd>,<Rs1(Opt)>,<shifter_operand>

## Slide 55
Operand 1
Result
ALU
Barrel Shifter
Operand 2
Operand 2 can also be taken from a register which can be optionally applied with shift operation.
Example: MOV, R0, R1, LSL #4
      R0: Operand 1
      R1: Operand 2
      #4: Shift value
The shift value can be either be:
  5 bit unsigned integer: Maximum shift of 32 positions
  Specified in the bottom byte of another register.
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>
Register Direct + Barrel Shifter

## Slide 56
The shift operation allows the operand to undergo some pre-processing before performing the actual arithmetic
Example:
  MOV, R0, R1, LSL #4 ; assume content of R1 = 0x12345678
  1. Get the value of R1 (R1 remains untouched)
  Original input = 0x12345678
  2. Shift the value left by 4 bits
  Processed input = 0x23456780
  3. Move the final value to R0
  R0 = 0x23456780
  R1 = 0x12345678
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>

## Slide 57
Does the using the barrer shifter incurs any additional cost?
When the immediate value of 5-bits field (Range = 0 to 31) is used for barrel shift
MOV R0, R1, ROR #4
  No performance overhead incurred
  Shift is done for free - executes in single cycle.
When the bottom byte of a register (not PC) is used
  MOV R0, R1, ROR R2
  Then takes extra cycle to execute
  ARM doesn’t have enough read ports to read 3 registers at once.
  Then, the performance is reduced to be similar to other processors where shift is separate instruction
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>

## Slide 58
What is the purpose of having the Barrel Shifter for Operand 2?
It’s free (not incurring any extra cost when properly used)
Shift is a common operation for many programs, e.g. DSP algorithms.
Multiplication instruction is typically much slower than addition in practice
Example: r0 = r1 * 13 Exa ple: r0 = r1 *(1 + 4 + 8)
Example: r0 = r1 + r1*4 + r1*8
Example: r0 = r1 + Shift_Left (r1, 2) + Shift_Left (r1, 3)
ADD r0, r1, r1, LSL #2 ; r0 = r1 + shift(r1, 2)
ADD r0, r0, r1, LSL #3 ; r0 = r0 + shift(r1, 3)
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>

## Slide 59
The ARM doesn’t have actual shift instructions.
Instead it has a barrel shifter which provides a mechanism to carry out shifts as part of other instructions
There are five types of barrel-shift operations:
  left shift (LSL)
  logical right-shift (LSR)
  arithmetic right-shift (ASR)
  Rotate right (ROR)
  Rotate right extended (RRX)
LSL, LSR, ASR and ROR are pseudo-instructions (not stand-alone) which are inserted as part of another primary instruction
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>

## Slide 60
Logical Shift Left (LSL)
Shifts left by the specified amount. The lower bits of the value are appended by 0. Value of shifter_operand remains unchanged
Destination
C
0
Example:
Assume that R1 = 0x0000 0003, R2 = 0x0000 0005
MOV R0, R1, LSL #2 | R0 = 0x0000 000C (3x4 = 12) R1 = 0x0000 0003 (unchanged)
MOV R0, R1, LSL R2 | R0 = 0x0000 0060 (3x32 = 96) R1 = 0x0000 0003 (unchanged)
  This is a simple way of performing a multiply by a power of 2 (x2n). For example, LSL #5 = multiply by 32
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 61
Logical Shift Right (LSR)
Shifts left by the specified amount. The lower bits of the value are appended by 0. Value of operand two remains unchanged
Example: Assume that R1 = 0x0000 000C, R2 = 0x0000 0003
MOV R0, R1, LSR #2 | R0 = 0x0000 0003 R1 = 0x0000 000C (unchanged)
MOV R0, R1, LSR R2 | R0 = 0x0000 0001 R1 = 0x0000 000C (unchanged)
  This is a simple way of performing an unsigned divide by a power of 2 (|÷2n|). For example, LSL #5 = divide by 32
Destination
C
0
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 62
Arithmetic Shift Right (ASR)
Shifts right (signed divide by powers of 2) by the specified amount & preserves the sign bit for 2's complement operations. E.g. ASR #5 = div by 32
Example:
Destination
CF
Arithmetic Shift Right
Sign bit shifted in
MOV R0, R1, ASR #2 or MOV R0, R1, ASR R2 where R2 = 2 | If R1 = 0x00000010  R0 = 0x0000 0004 if R1 = 0xFFFF FFF0  R0 = 0xFFFF FFFC R1 remains unchanged
Shifter Operand 3: Register Direct + Barrel Shifter
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>

## Slide 63
Rotate Right (ROR)
Similar to an ASR but the bits wrap around as they leave the LSB and appear as the MSB. The last bit to be shifted out is also used as the carry out
Example: Assume that R1 = 0x8000 0002, R2 = 0x0000 0003
Destination
C
Rotate Right
Shifter Operand (3.4)
Instruction <Rd>,<Rs1 (Opt)>,<shifter_operand>,<shift>
MOV R0, R1, LSL #2 | R0 = 0xA000 0000 R1 = 0x8000 0002 (unchanged)
MOV R0, R1, LSL R2 | R0 = 0x5000 0000 R1 = 0x8000 0002(unchanged)
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 64: Example 1
Description:
Write a procedure which performs the following operation
Y = 20*X1 + X2
Input: M[X1] = 2, M[X2] = 3
Output: M[Y]
Write the assembly code to perform the following task:

## Slide 65
TTL func1_slow
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, X1 ; Load content of X1 into R0
LDR R1, X2 ; Load content of X2 into R1
MOV R2, #20 ; R2 = 20 (for multiplication)
MUL R3, R0, R2 ; R3 = 20X1 (Register Direct)
ADD R4, R3, R1 ; R4 = 20X1 + X2 (Immediate)
STR R4, Y ; Save result into Y
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X1 DCD 2 ; input 1
X2 DCD 3 ; input 2
Y DCD 0 ; output
END
But MUL is slow!!!!

## Slide 66
The instruction “MUL R3, R0, #20” or 20X1 can be converted into a series of shift operations as follows
R3 = R0 * 20
e: r0 = R0 *(4 + 16)
  = R0*4 + R0*16
  = LSL(R0, 2) + LSL (R0, 4)
Instructions:
    MOV R2, #20 
    MUL R3, R0, R2
Alternative way:
  MOV R3, R0, LSL #2
  ADD R3, R3, R0, LSL #4

## Slide 67
TTL func1_fast
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, X1 ; Load content of X1 into R0
LDR R1, X2 ; Load content of X2 into R1
MOV R3, R0, LSL #2 ; 4*X1 (Barrel Shift)
ADD R3, R3, R0, LSL #4 ; 4*X1 + 16*X1 ( Barrel Shift)
ADD R3, R3, R1 ; 20X1 + X2 (Register Direct)
STR R3, Y ; Save result into Y
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X1 DCD 2 ; input 1
X2 DCD 3 ; input 2
Y DCD 0 ; output
END

## Slide 68: Example 2
Description:
Write a procedure which performs the second order complement of -X
Y = 2ndComplement (X)
Input: M[X] = 0x00010001
Output: M[Y]
Write the assembly code to perform the following task:

## Slide 69
TTL secondcomp
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, X ; Load content of X into R0
MVN R0, R0 ; Invert all bits in R0
ADD R0, R0, #1 ; Add 1 to inverted bits
STR R0, Y ; Store result
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X DCD 0x0001 0001 ; input
Y DCD 0 ; output
END

## Slide 70: ADDRESSING MODES

## Slide 71
Programs use data structures to organize the information used in computations
One common example is a table containing N integers which are stored in a contiguous memory segment
Addressing Modes
LDR/STR <Rd>,<addressing_mode>
Base Address
Memory
5
11
12
2
0x200C
0x200
Base Address + 12
How to get the fourth integer from the table?
  Provide the absolute address  not flexible
  Provide the base address of the table + offset  Need only to change the base address if table is loaded elsewhere in the memory
Addressing modes provide different ways to specify the operand locations w.r.t. a base address
***Only applicable to LDR and STR

## Slide 72
Name | Syntax | Addressing Function | Example
Register indirect | [Ri] | EA = [Ri] | LDR R0, [R1]
Pre-Indexed Pre-indexed with WriteBack Post-indexed Relative | [Ri, X] [Ri, X]! [Ri], X Label | EA = [Ri] + X; Rk unchanged EA = [Ri]+ X, Rk  Rk + X EA = [Ri]; Rk  Rk + X EA = [PC] + offset | LDR R0, [R1, #4] LDR R0, [R1, #4]! LDR R0, [R1], #4 BRA Label
EA = Effective Address
X = index/offset value
Label = a label pointing to the memory location
Addressing Modes
LDR/STR <Rd>,<addressing_mode>

## Slide 73
Register Indirect
Immediate and Register addressing mode does not handle memory access.
Data transfer between the system memory and a register in the CPU is handled by the LDR and STR instructions only.
The indirect mode is used to access the location of the memory. The location to be accessed is stored in a register where the register plays the role of a pointer.
The Indirect mode provides address in register:
LDR R2, [R5] ; R2  M[R5]
Register Indirect
LDR/STR <Rd>,<addressing_mode>

## Slide 74
0x1111 2222
0x23AB 2345
R0
Main Memory
0x1000
0x00001000
AREA Code, CODE, READONLY
LDR R0, =Value1
LDR R1, [R0]
…
AREA Table1, DATA, READWRITE
Value 1 DCD 0x11112222
DCD 0x23AB2345
END
R1
0x11112222
Value1
1) MOV R0, Value1
2) LDR R1, [R0]
Register Indirect
LDR/STR <Rd>,<addressing_mode>
Register Indirect
Table1

## Slide 75
Pre-indexed mode: LDR R0, [R1, Offset]
The effective address of the operand is the sum of the contents of the base register Rn and an offset value
Pre-indexed with writeback mode: LDR R0, [R1, Offset]!
The effective address of the operand is generated in the same way as in the Pre-indexed mode, and then the effective address is written back into Rn
Post-indexed mode: : LDR R0, [R1], Offset
The effective address of the operand is the contents of Rn. The offset is then added to this address and the result is written back into Rn
Register Indirect + Indexed
LDR/STR <Rd>,<addressing_mode>
Register Indirect + Indexed

## Slide 76
Register Indirect + Indexed
LDR/STR <Rd>,<addressing_mode>

## Slide 77
Mechanism to provide indexed access to a table. Allows easy access to a particular item in the table. For example, to access the forth item in a table with base register:
STR r0, [r1,#12]
The offset register (R1 in this example) is not changed after instruction execution
This addressing mode avoids hard-coding. When the table is moved to a different location, we simply need to update the base register with the new table starting address
r1
0x200
Base Register
Memory
0x5
0x20c
r0
0x5
Source Register for STR
Offset
12
0x200
Pre-indexed Addressing Mode
Pre-indexed
LDR/STR <Rd>,<addressing_mode>

## Slide 78
More examples:
LDR R0, [R1, #4]
LDR R0, [R1, R2]
LDR R0, [R1, R2, LSL#2]
R0  M[R1+4].
Registers R1 are not changed
R0  M[R1+R2]
Registers R1 and R2 are not changed
R1  M[R1 + LSL(R2, 2)]
Registers R1 and R2 are not changed
Pre-indexed Addressing Mode
Pre-indexed
LDR/STR <Rd>,<addressing_mode>

## Slide 79
Same as Pre-indexed addressing Mode. The difference is that the offset register will be updated after the operation is completed.
STR r0, [r1,#12]!
The offset register (R1 in this example) is updated after the operation
R1  R1 + offset
Useful to implement a loop to perform sequential access to all items in the table
+
r1
0x200
Base Register
Memory
0x5
0x20c
r0
0x5
Source Register for STR
Offset
12
0x200
Pre-indexed Addressing Mode with WriteBack
Pre-indexed with WriteBack
LDR/STR <Rd>,<addressing_mode>

## Slide 80
More examples:
LDR R0, [R1, #4]!
LDR R0, [R1, R2]!
LDR R0, [R1, R2, LSL #2]!
R0  M[R1+4]
R1  R1 + 4
R0  M[R1+ R2]
R1  R1 + R2
R2 is unchanged
R0  M[R1+LSL(R2,2)]
R1 R1 + LSL(R2, 2)
R2 is unchanged
Pre-indexed Addressing Mode with WriteBack
Pre-indexed with WriteBack
LDR/STR <Rd>,<addressing_mode>

## Slide 81
r1
0x200
Original Base Register
Memory
0x5
0x20c
r0
0x5
Source Register for STR
Offset
12
0x200
r1
0x20c
Updated Base Register
Different from pre-indexed addressing mode, in post-indexed addressing, the effective address is not modified by the offset.
STR r0, [r1] , #12
The offset register is updated only after the operation
R1  R1 + offset
Post-indexed Addressing Mode
Post-Indexed
LDR/STR <Rd>,<addressing_mode>

## Slide 82
More examples:
LDR R0, [R1], #4
LDR R0, [R1], R2
LDR R0, [R1], R2, LSL #2
R0  M[R1]
R1  R1 + 4
R0  M[R1]
R1  R1 + R2
R2 is unchanged
R0  M[R1]
R1  R1 + LSL(R2,2)
R2 is unchanged
Post-indexed Addressing Mode
Post-indexed
LDR/STR <Rd>,<addressing_mode>

## Slide 83: Example 1
Description:
Write a procedure which adds all items in a table of data (word size).
Input:
M[X] = 0x2, 0x6, 0xA (table)
Output:
M[Y] (sum of items)
Write the assembly code to perform the following task:

## Slide 84
TTL AddTable
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =X ; R0 = X = start of table
LDR R1, [R0], #4 ; R1 = X[0] (post-increment)
LDR R2, [R0], #4 ; R2 = X[1] (post-increment)
LDR R3, [R0] ; R2 = X[2]
ADD R1, R1, R2 ; R1 = X[0] + X[1]
ADD R1, R1, R3 ; R1 = (X[0] + X[1]) + X[2])
STR R1, Y ; save result to Y
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X DCD 0x2, 0x6, 0xA ; input
Y DCD 0 ; output
END

## Slide 85: Example 2
Description:
Write a procedure to copy two consecutive items indexed by IDX and item IDX+1 from array M[X] in a table and saves them into array M[Y]
Input:
M[X] = 0x2, 0x6, 0xA, 0x3, 0x6 (5-item array)
M[IDX] = 2 (third and fourth items)
Output:
M[Y] (2-item array)
Write the assembly code to perform the following task:

## Slide 86
TTL CopyTwoIndexedItems
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =X ; R0 = X = base addr of source table
LDR R1, =Y ; R1 = Y = base addr of target table
LDR R2, IDX ; R2 = IDX = 2
LDR R3, [R0, R2, LSL #2]! ; R0 = base + 4*index, or
; R0 = R0 + 4*R2
; R2 = M[R2] = third item in X = 0xA
LDR R3, [R0, #4]! ; R3 = M[R0+4] = fourth item in X = 0x3
STR R2, [R1], #4 ; Y[0] = R2, R1 = R1 + 4
STR R3, [R1] ; Y[1] = R3
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
IDX DCD 2 ; input index
X DCD 0x2, 0x6, 0xA, 0x3, 0x6 ; input array
Y DCD 0, 0 ; output array
END

## Slide 87: ASSEMBLY DIRECTIVE GROUP
  EQU, AREA, DCB, DCW, DCD, ALIGN, ENTRY, END

## Slide 88: Assembler Directives
An assembler directive tells the assembler something it needs to know in order to carry out the assembly process.
Similar to Preprocessor directives in C-Programming.
Common assembler directives:-
  <label> EQU <value> Equate (label is equated with value)
  AREA <value> Define an area in the program (code/data)
  <label> DCB <value> Define constant (byte)
  <label> DCW <value> Define constant (half-word)
  <label> DCD <value> Define constant (word)
  ALIGN Ensure the next data is aligned to word boundary
  ENTRY Specify the entry to the whole program
  END End of program

## Slide 89: <label> EQU <expr>
EQU equates a symbolic name to a numeric value.
Example
TTL PROG1
    Length EQU 16 ; decimal number
    Width1 EQU 0x10 ; 0x: hexadecimal number
    Width2 EQU 2_10000 ; 2_: binary number
    Width2 EQU 8_20 ; 8_: octal number
    AREA Program, CODE, READONLY
    …
    MOV R1, #Length ; equivalent to LDR R1, #16
    MOV R2, #Width ; EQU simply replaces the label
  Advantages:
  The code does not have to be modified even if the values of Length and Width are changed.

## Slide 90: AREA <name>, <atr> <atr>, ENTRY, END
AREA establishes indivisible memory regions that are manipulated by the linker. Key attributes include
  CODE: area includes only instruction
  DATA: area includes only data
  READONLY: default for CODE areas
  READWRITE: default for DATA areas
ENTRY indicates the point in the code where program execution should begin. There should be only ONE entry point per complete program.
END tells the assembler that the end of a program is reached.
  AREA Prog1, CODE, READONLY ; define a new code region labeled as Prog1
  ENTRY ; Entry point for program
  … ; code write your code here
  AREA Table1, DATA , READWRITE ; define a new data region labeled as Table1
  … ; data goes here
  END ; End of program

## Slide 91: <label> DCD <expr>
DCD allows you to put a data value in memory at the time that the program is first loaded.
  A DCD 0x00BB 00AA
  B DCD 0x00CC 00CC
  C DCD 0x12, 0x13, 0x14
4000
4004
4008
400C
4010
4010
400C
00BB
00CC
0000
0000
0000
00AA
00DD
0012
0013
0014
DCD allocates words (32 bit) of memory, padding as necessary to ensure word alignment and initializes them to the values given
A, B and C is actually pointers (point to a memory address). The actual value of A = 0x4000 and B = 0x4004. The content pointed by A or M[A] is 0x00BB 00AA

## Slide 92: <label> DCW/DCB <expr>, ALIGN
4000
4004
4008
400C
4010
4010
400C
BBBB
4142
CCCC
AA
43
CCCC
DCW allocates half-words (16 bit) of memory and initializes it with the value
DCB allocates byte (8 bytes) of memory
ALIGN e-aligns the data so that the next data will be aligned to the word boundary
  A DCW 0xBBBB
  B DCB 0xAA
  ALIGN
  C DCB “ABC”
  ALIGN
  D DCD 0xCCCCCCCC
00
00

## Slide 93: DATA TRANSFER GROUP
  Register to Register (MOV, MVN)
  Memory to Register (LDR, LDM)
  Register to Memory (STR, STM)

## Slide 94: MOV<cond><s> <Rd>,<Shifter Operand>
Performs a move to a register (Rd) the content from another register (with barrel shift) or an immediate value (32 bit)
Flags updated if S used and Rd is not R15: N, Z and C
Example:
    MOV R1, R0, LSL #2 ;R1 <- R0*4
    Status flags not updated
    MOVS R1, #0 ;R1<- 0x00000001
    Status flags – N:0, Z:1, V:0, C:0
    MOVSNE R0, #0x4
    if status flag N = 0, the R0  0x00000004
    If status flag N = 1, instruction is ignored

## Slide 95: MVN<cond><s> <Rd>,<Shifter Operand>
MVN complements the value of a register or an immediate value and stores it in the destination register (Rd)
Flags updated if S used and Rd is not R15: N, Z and C
Example:
    MVN R1, R0, LSL #2 ;R1 <- NOT(R0*4)
    Status flag is not updated
    MVNS R1, #1 ;R1<- FFFFFFFE
    Status flags – N:1, Z:0, V:0, C:0

## Slide 96: LDR<cond> <Rd>,<addressing_mode>
Load operand from memory (Index Mode) into target register (Rd)
  LDR: Load 32 bits
  LDRH: Load halfword (16 bit unsigned #) & zero-extend to 32 bit
  LDRSH: Load halfword (16 bit unsigned #) & sign-extend to 32 bit
  LDRB: Load byte (8 bit unsigned #) & zero-extend to 32 bit
  LDRBH: Load byte (9 bit unsigned #) & sign-extend to 32 bit
No <S> field: status register will not be updated by LDR instruction

## Slide 97
Example of LDR indexed addressing modes:
  indirect: LDR r0, [r1] ;r0  M[r1]
  Preindexed LDR r0, [r1, -r2] ;r0  M[r1-r2]
  Preindexed+WB LDR r0, [r1, #4]! ;r0  M[r1+4], r1 r1+4
  Post-indexed LDR r0, [r1], #4 ;r0  M[r1], r1  r1 + 4
  Example:
  LDRS r0, [R1] ;if M[R1]=0 N=0, Z=1, C=0, V=0
  LDRSCC r0, [r1] ;conditional execution if carry is clear
        ;update SR

## Slide 98: LDR<cond> <Rd>,<label> LDR<cond> <Rd>,=<label>
When loading a variable defined by a symbol (assuming the data area starts at 0x1000):
  LDR R0, =A ; R0 = 0x1000
  LDR R1, [R0] ; R1 = M[A] = 0x2
  …
  LDR R1, A ; R1 = M[A] = 0x2
  AREA Table1, DATA, CODE
  A DCD 0x2
  END

## Slide 99: STR<cond> <Rs>,<addressing_mode>
Load operand from source register (Rs) into memory (R, Index)
  STR: Store 32 bits
  STRH : Store halfword (right-most 16 bit)
  STRB: Load halfword (rightmost 8 bit)
No <s> field: status register is not affected by STR
Example:
  STR R0, [R1], -R2, LSL#2 ; M[R1] = R0, R1 = R1 – (R2*4)
  STR R0, [R1, #4] ; M[R1+4] = R0, R1 unchanged

## Slide 100: STR<cond> <Rd>,<label>
When loading a variable defined by a symbol (assuming the data area starts at 0x1000):
  MOV R0, #12 ; R0 = 12
  STR R0, Result ; M[Result] = 12
  AREA Data, DATA, CODE
  Result DCD 0
  END

## Slide 101: LDM<cond> Rs<!>, <list of Rd>
Perform a block transfer of multiple words from the memory into several target registers
  LDMIA – increment address by 4 after each load
  LDMDA – decrement address by 4 before each load
  LDMIB – increment address by 4 before each load
  LDMDB – decrement address by 4 before each transfer
No <S> field: status register is not affected by LDM
<!> specifies if Rs is updated after operation (updated if ! Is present)
Addressing Mode | Description | Start Address | End Address | Rs!
IA | Increment after | Rs | Rs + 4*¦Rd¦- 4 | Rs+4*¦Rd¦
IB | Increment Before | Rs + 4 | Rs + 4*¦Rd¦ | Rs+4*¦Rd¦
DA | Decrement After | Rs – (4*¦Rd¦+4) | Rs | Rs-4*¦Rd¦
DB | Decrement Before | Rs – (4*¦Rd¦) | Rs – 4 | Rs-4*¦Rd¦

## Slide 102
Examples:
  LDMIA R7, {R0, R2-R4} ; R0 = M[R7]
            ; R2 = M[R7+4]
            ; R3 = M[R7+8]
            ; R4 = M[R7+12]
            ; R7 is unchanged
  LDMDB R7!, {R0, R2-R4} ; R0 = M[R7-16]
            ; R2 = M[R7 - 12]
            ; R3 = M[R7 - 8]
            ; R4 = M[R7 - 4]
            ; R7 = R7 - 16

## Slide 103
Examples:
  LDMIA R7, {R0, R2-R4} ; R0 = M[R7]
            ; R2 = M[R7+4]
            ; R3 = M[R7+8]
            ; R4 = M[R7+12]
            ; R7 is unchanged
  LDMDB R7!, {R0, R2-R4} ; R0 = M[R7-16]
            ; R2 = M[R7 - 12]
            ; R3 = M[R7 - 8]
            ; R4 = M[R7 - 4]
            ; R7 = R7 - 16

## Slide 104: STM<cond><Rd><!>, <list of Rs>
Perform a block transfer of multiple words from several source registers into memory
  STMIA – increment address after transfer
  STMMDA – decrement address after transfer
  STMMIB – increment address before transfer
  STMDA – decrement address before transfer
No <S> field: status register is not affected by LDM

## Slide 105
Examples:
STMIA R7, {R0, R2-R4} ;memory[R7]  R0
          ;memory[R7+4]  R2
          ;memory[R7+8]  R3
          ;memory[R7+12]  R4
          ;R7 is unchanged
STMDB R7!, {R0, R2-R4} ;memory[R7-16]  R0
;memory[R7-12]  R2
;memory[R7-8]  R3
;memory[R7-4]  R4
;R7  R7 - 16

## Slide 106: Example 1
Description:
Write a procedure to copy an array of five items (word size) from memory location to another array at memory location Y
Input:
M[X] = 0x2, 0x6, 0xA, 0x3, 0x6 (5-item array)
Output:
M[Y] (5-item array)
Write the assembly code to perform the following task:

## Slide 107: Example 1
TTL CopyArrays
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =X ; R0 = X = source table base
LDR R1, =Y ; R1 = Y = target table base
LDMIA R0, {R2-R6} ; Copy X to R2toR6
STMIA R1, {R2-R6} ; Copy R2toR6 to Y
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X DCD 0x2, 0x6, 0xA, 0x3, 0x6 ; input array
Y DCD 0, 0, 0, 0, 0 ; output array
END

## Slide 108: Example 2
Description:
Write a procedure to swap the first two contents of an array with the last two items of the array A
Input:
M[A] = 0x2, 0x6, 0xA, 0x3 (4-item array)
Output:
M[A] = 0xA, 0x3, 0x2, 0x6
Write the assembly code to perform the following task:

## Slide 109: Example 2
TTL SwapItems
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =A ; R0 = A
LDMIA R0, {R2-R5} ; Copy A to R2toR5
STMIA R0!, {R4-R5} ; Copy R4toR5 to top half of A
STMIA R0!, {R2-R3} ; Copy R2toR3 to bottom half of A
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x2, 0x6, 0xA, 0x3 ; array
END

## Slide 110: Example 3
Description:
Write a procedure to swap the array A with array B. Both array contains 12 items
Input:
M[A] = 0x1, 0x2, 0x3, 0x4, 0x5, 0x6, 0x7, 0x8, 0x9, 0x0, 0x1, 0x2
M[B] = 0x11, 0x12, 0x13, 0x14, 0x15,0x16, 0x17, 0x18, 0x19, 0x10,
0x11, 0x12
Output:
M[A] is swapped with M[B]
Write the assembly code to perform the following task:

## Slide 111: Example 3
TTL SwapArray
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =X ; R0 = X = source table base
LDR R1, =Y ; R1 = Y = target table base
LDMIA R0, {R2-R7} ; Copy X[0:5] to R2-R7
LDMIA R1, {R8-R13} ; Copy Y[0:5] to R8-R13
STMIA R1!,{R2-R7} ; Copy R2-R7 (storing X[0:5]) to Y[0:5], Point to Y[6]
STMIA R0!,{R8-R13} ; Copy R8-R13 (storing Y[0:5]) to X[0:5], Point to X[6]
LDMIA R0, {R2-R7} ; Copy X[6:11] to R2-R7
LDMIA R1, {R8-R13} ; Copy Y[6:11] to R8-R13
STMIA R1!,{R2-R7} ; Copy R2-R7 (storing X[6:11]) to Y[6:11], Point to Y[12]
STMIA R0!,{R8-R13} ; Copy R8-R13 (storing Y[6:11]) to X[6:11], Point to X[12]
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
X DCD 0x1, 0x2, 0x3, 0x4, 0x5, 0x6, 0x7, 0x8, 0x9, 0x0, 0x1, 0x2
Y DCD 0x11, 0x12, 0x13, 0x14, 0x15, 0x16, 0x17, 0x18, 0x19, 0x10, 0x11, 0x12
END

## Slide 112: ARITHMETIC GROUP
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  MUL operand1 * operand2

## Slide 113: ADD<cond><s> <Rd>,<Rs1>,<Shift Operand>
Rd  Rs1 + Shifter Operand
Flags updated if S is used: N, Z, V, C
Examples:
  ADDS R4, R2, R0 ; R4 R2 + R0 & update CPSR
  ADD R5, R3, R1 ; R5  R3 + R1
  ADD R5, R3, R1, LSL #2 ; R5 R3 + Logical_Shift_Left ; of R1 by 2

## Slide 114: ADC<cond><s> <Rd>,<Rs1>,<Shift Operand>
Addition with carry: Rd  Rs1 + Shifter Operand + C
The value of C is determined by previous instructions
Flags updated if S is used: N, Z, V, C
The ADC instruction is used to implement efficient multiword addition. For example, if 64-bit numbers are stored in R1:R0 and R3:R2, their sum can be stored in R5:R4 as shown below.
  ADDS R4, R2, R0 ; add the least significant word ; field <S> will update the carry bit
  ADC R5, R3, R1 ; add the most significant word

## Slide 115: SUB<cond><s> <Rd>,<Rs1>,<Shift Operand>
Rd  Rs1 - Shifter Operand
Flags updated if S is used: N, Z, V, C
Examples:
  SUBS R0, R0, #1 ; decrement R0 by 1, update flags
  SUB R0, R2, R1 ; R0  R2 – R1
  SUB R0, R2, R1, LSR #2 ; R0  R2 – Logical_shift_right
  ; of R1 by 2

## Slide 116: SBC<cond><s> <Rd>,<Rs1>,<Shift Operand>
Subtract with carry: Rd  Rs1 - Shifter Operand – NOT C
The value of C is determined by previous instructions.
For subtraction, ARM clears the carry if the result is less than 0 (borrow required). The carry flag (C) is the inverse of a borrow flag. Therefore, if a borrow is required by the operation, C will be set to 0 and SBC will subtract an additional one from current value.
Flags updated if S is used: N, Z, V, C
The SUB instruction is used to implement efficient multiword subtraction. For example, if 64-bit numbers are stored in R1:R0 and R3:R2, their difference can be stored in R5:R4 as shown below.
SUBS R4, R2, R0 ; subtract least significant words
SBC R5, R3, R1 ; subtract most significant words minus borrow

## Slide 117: MUL<cond><s> <Rd>,<Rs1>,<Shift Operand>
Rd  Rs1 * Shift_Operand
Flags updated if S is used: N, Z
MUL performs a 32x32 operation, and stores the lower 32 bit of the result into Rd.
Since only the least significant 32-bits are stored, the result may not be the complete  Suitable only for half-word. To overcome this instruction, use the UMULL instruction.
Example:
  MUL R0, R1, R2 ;R0  R1*R2

## Slide 118: LOGICAL OPERATION
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2

## Slide 119: AND, EOR, ORR, BIC <cond><s> <Rd>,<Rs1>,<Shift Operand>
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Shift_Operand
Flags updated if S used: N, Z, C
Logical operations can be used to manipulate the data. Examples:
  AND R0, R0, #0x8000 ; mask bit D15 of R0
  EOR R0, R0, #0x8000 ; toggle bit D15 of R0
  ORR R0, R0, #0x8000 ; set bit D15 of R0
  BIC R0, R0, #0x8000 ; clears bit D15of R0

## Slide 120: Example 1
Description:
Write a procedure to add three numbers in memory location Table. Store the result in memory location Result.
Input:
M[Table] = 0x1, 0x3, 0x4 (3-item array)
Output:
M[Result]
Write the assembly code to perform the following task:

## Slide 121
TTL Add3No
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =Table ; Initialize R0 to start of table
LDMIA R0, {R1-R3} ; Get three numbers
ADD R4, R1, R2 ; Add the first and second number
ADD R4, R4, R3 ; Add the third number
STR R4, Result ; Store result
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
Table DCD 0x1, 0x3, 0x4 ; array
Result DCD 0 ; result
END

## Slide 122: Example 2
Description:
Write a procedure to add two long words in memory location A and B, respectively. Store the result in memory location Result.
Input:
M[A] = 0x20002000F000F000 (3-item array)
M[B] = 0x3000300010001000
Output:
M[Result]
Write the assembly code to perform the following task:

## Slide 123
TTL AddLongNumbers
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, =A ; Initialize R0 to MSB of A
LDMIA R0, {R1-R2} ; MSW  R1, LSW R2
LDR R0, =B ; Initialize R0 to MSB of B
LDMIA R0, {R3-R4} ; MSW  R3, LSW  R4
ADDS R6, R2, R4 ; Add the LSW (Update CPSR)
ADC R5, R1, R3 ; Add the MSB and carry from LSW
LDR R0, =Result ; Initialize R0 to MSB of Result
STMIA R0, {R5-R6} ; Store long word result to Result
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x20002000, 0xF000F000
B DCD 0x30003000, 0x10001000
Result DCD 0, 0 ; result
END

## Slide 124: Example 3
Description:
Given a five bit binary code stored in the lowest four bits of M[A], convert the binary code into a gray code
Input:
M[A] = 0x0000000B (Binary Code)
Output:
M[B] = 0x0000000E (Gray Code)
Write the assembly code to perform the following task:

## Slide 125
TTL ConvertToGrayCode
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, A ; Initialize R0 = M[A] = 10112
AND R2, R0, #2_1000 ; R2 = get bit 3  R2 stores bit 3
AND R3, R0, #2_0100 ; R3 = get bit 2
AND R4, R0, #2_0010 ; R4 = get bit 1
AND R5, R0, #2_0001 ; R5 = get bit 0
EOR R6, R3, R2, LSR #1 ; R6 = bit 2 XOR bit 3 R6 stores bit 2
EOR R7, R4, R3, LSR #1 ; R7 = bit 1 XOR bit 2  R7 stores bit 1
EOR R8, R5, R4, LSR #1 ; R8 = bit 0 XOR bit 1  R8 stores bit 0
ORR R2, R2, R6 ; Accumulate all bits
ORR R2, R2, R7
ORR R2, R2, R8
STR R2, B
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 0x0000000B
B DCD 0
END

## Slide 126: COMPARISON GROUP
  CMP TST TEQ

## Slide 127: Comparison Group
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 128: CMP<cond> <Rn>,<shifter operand>
The CMP instruction performs a subtraction, but does not store the result. The flags are always updated.
Rn – Shifter_operand
Examples:
  CMP R0, #1 ; Z=1 if R0 = 1, Z = 0 if R0 > 1
  CMP R0, R1 ; Z =1 if R0 = R1, Z = 0 if R0 > R1

## Slide 129: TST <cond> <Rn>,<shifter_operand>
The TST instruction performs a non-destructive AND (the result is not stored). The flags are always updated.
The most common use for this instruction is to determine the value of an individual bit of a register.
Rn AND shifter_operand
Examples:
  TST R0, #0x8000 ;if bit 15 of R0 = 0, set Z = 1

## Slide 130: TEQ <cond><Rn>,<shifter_operand>
The TEQ instruction performs a non-destructive bit-wise XOR (the result is not stored). The flags are always updated.
The most common use for this instruction is to determine if two operands are equal without affecting the V flag. If equal, Z = 1
It can also be use to tell if two values have the same sign, since the N flag will be the logical XOR of the two sign bits.
Rn XOR shifter_operand
Examples:
TEQ R0, #0x8000 ; Z = 1 if R0 = 0x00008000
TEQ R0, R1 ; N = 1 if the signs are different

## Slide 131: FLOW CONTROL GROUP
B, BL (not covered)

## Slide 132: Flow Control Group
…
MOV R0, #3
BAL LABEL
ADD R0, R1, R2
…
LABEL …
0x0010
0x002C
0x000C
In general, an instruction is executed in sequence until it bumps into a branch instruction.
If the instruction in 0x0010 is not BAL, the sequence of value for Program Counter (PC) is 0x0010  (0x0010 + 4 = 0x0014)  0x0018
With the BAL (always branch) instruction, the sequence of value for PC becomes 0x0010  0x002C where 0x002C is the address of the target destination label

## Slide 133: Flow Control Group
B:
  Branch to the location specified by the label
  Does not affect the Link Register (LR)
  Used to implement loop or if-else statements
BL (not covered):
    Used to implement functions (to remember the caller function and location, so that it can return to the right place after running the called function)
    Similar to B but additionally save the value PC-4 into LR of the current bank: BL LOCATION_LABEL
    To return from subroutine, simply restore the PC from the Link Register: MOV PC, LR

## Slide 134: B<cond> <target address>
A branch instruction tests a branch condition and then, depending on the result, causes execution to proceed along one of two possible paths.
The branch conditions are related to the result of a recently performed operation which updates the status register
N = Negative result from ALU flag.
Z = Zero result from ALU flag.
C = ALU operation Carried out
V = ALU operation oVerflowed
* Condition Code Flags
Mode
N
Z
C
V
28
31
8
4
0
I F T

## Slide 135: B<cond> <target address>
The B<cond> instructions are used to branch to a target address, based on an optional condition <cond>. Possible values for <cond> are as follows:

## Slide 136: Accessing items in an table or array
The branch instruction is very useful for a lot of cases. One such cases processing repeated items such as an array
For example, let’s say we want to add numbers in a table:
The most naïve way is to write the following code :
  LDR R1, =Table
  ADD R0, [R1], #4
  ADD R0, [R1], #4
  ADD R0, [R1], #4
  ADD R0, [R1], #4
  …
Table | 3
 | 2
 | 13
 | 4
But what if we have 1000 data? (Not a practical solution)

## Slide 137: Accessing items in an table or array
  Solution: use a loop.
    Put the repetitive code (load and addition) into a loop. Each iteration adds one number.
    Use a variable to store the total summation value
    Use a variable to store the unprocessed item in table
    Use a counter to keep track of how many items has been processed. Exit loop once all items has been processed
      initialize sum = 0, i = N (#item),
  repeat
  sum = sum + item (N – i + 1) ; add item i to sum
  i = i - 1 ; point to next item
  if i == 0, exit from loop ; all item done?
  end

## Slide 138: Accessing items in an table or array
    Use R0 to keep track of how many items has been processed.
    Use R2 to store the address of current item during each iteration
    Use R3 to store the current item
    Use R1 to sum one item at a time.
      R0  N
  R1  0
  R2  Start of Table
  REPEAT
  R3  M[R2] ; get item i
  R1  R1 + R3 ; sum item i to sum
  R2 = R2 + 4 ; i = i + 1
  R0 = R0 - 1 ; decrement counter
  UNTIL R0 == 0
Pseudo-code:

## Slide 139: Accessing items in an table or array
  MOV R0, N ; R0 = #items
  LOOP …
  SUBS R0, #1 ; decrement counter R0
  BNE LOOP ; repeat if R0 != 0
  …
  Pseudo-code
  Assembly code (only branch related instructions are shown)
      R0  N, R1  0, R2  Start of Table
  REPEAT
  R3  M[R2] ; get item i
  R1  R1 + R3 ; sum item i to sum
  R2 = R2 + 4 ; i = i + 1
  R0 = R0 - 1 ; decrement counter
  if R0 == 0, exit from loop
  END

## Slide 140: If-Else Statements
The branch instruction can be used to implement the if-else statements
Example:
      if x == 0
      y = 2;
      else
      y = 3;
      CMP R0, #0 ; R0 holds x, R1, holds y
      BNE CASE2 ; if x == 0
      CASE1 MOV R1, #2 ; case 1 (yes)
      BAL NEXT
      CASE2 MOV R1, #3 ; case 2 (no)
      NEXT ….

## Slide 141: If-Else Statements
A better way to implement the if-else statement without using the branch instructions
Example:
      if x == 0
      y = 2;
      else
      y = 3;
      CMP R0, #0 ; R0 holds x, R1, holds y
      MOVEQ R1, #2 ; case 1
      MOVNE R1, #3 ; case 2

## Slide 142: While Statements
      while(i != j)
      {
      if (i > j)
      i--;
      else
      j--;
      }
      LOOP CMP R0, R1 ; set condition "NE" if (i != j),
      ; "GT" if (i > j),
      ; "LT" if (i < j)
          SUBGT R0, R0, #1 ; if "GT" (greater than), i = i-1;
          SUBLT R1, R1, #1 ; if "LT" (less than), j = j-1;
          BNE LOOP ; if "NE" (not equal), then loop

## Slide 143: Example 1
Description:
Get the factorial of a number A. Store the result in RESULT
Input:
  M[A] = 4
Output:
M[RESULT]
Write the assembly code to perform the following task:

## Slide 144: Example 1
RESULT = A;
for (int i=N-1; i>0; i--)
{
RESULT = RESULT *i
}
FACT  A ; R0
NEXT  A – 1 ; R1
REPEAT
FACT  FACT * NEXT
NEXT  NEXT – 1
Until NEXT = 0
M[RESULT] = FACT

## Slide 145: Example 1
TTL factorial
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, A ; R0 = A
SUBS R1, R0, #1 ; R1 = A - 1
LOOP MULNE R0, R1, R0 ; multiply as long as R1 > 0
SUBS R1, R1, #1 ; decrement counter
BGT LOOP ; if item > 0, carry on
STR R0, RESULT ; Store result to M[RESULT]
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
A DCD 4
RESULT DCD 0
END

## Slide 146: Example 2
Description:
Given an array ARR of integers of size N, find the maximum value in ARR. Store the result in RESULT
Input:
  M[N] = 5
  M[ARR] = -2, 9, 121,-222, 5
Output:
M[RESULT]
Write the assembly code to perform the following task:

## Slide 147: Example 2
RESULT = ARR[0]; // R2  MAX (intialize to 1st item)
for (int i=N; i>0; i--) // R0  i,
{
item = ARR[i|; // R3  item
// R1  pointer of ARR[i]
if (item > MAX)
MAX = item;
}

## Slide 148: Example 2
i  N ; R0 to store counter
pointer  ARR ; R1 to point to current item in table
MAX  M[pointer] ; R2 to store the maximum number
REPEAT
ITEM  M[pointer] ; R3 to store current item
pointer  pointer + 4 ; update pointer to next item
IF ITEM > MAX
MAX  ITEM ; new maximum value if ITEM > MAX
END IF
i  i – 1 ; decrement counter
Until i = 0
M[RESULT] = MAX

## Slide 149: Example 2
TTL GetMaximumNum
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, N ; R0 = counter
LDR R1, =ARR ; R1 = pointer to table
LDR R2, [R1] ; R2 = MAX (initialize to ARR[0])
LOOP LDR R3, [R1], #4 ; R3 = current item, update pointer
CMP R2, R3 ; Compare current item with MAX
MOVLT R2, R3 ; if current item > MAX, update MAX
SUBS R0, #1 ; decrement counter
BNE LOOP ; check if all items have been processed
STR R2, RESULT ; Store result to M[RESULT]
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
N DCD 5
ARR DCD -2, 9, 121,-222, 5
RESULT DCD 0
END

## Slide 150: Example 3
Description:
Given an array ARR of integers of size N, find the number of negative values in ARR. Store the result in RESULT
Input:
  M[N] = 5
  M[ARR] = -2, 9, 121,-222, 5
Output:
M[RESULT]
Write the assembly code to perform the following task:

## Slide 151: Example 3
NUMNEG = 0; // NUMNEG -> R1
for (int i=N; i>0; i--) // i -> R0,
{
item = ARR[i|; // item -> R2, addr of ARR[i] -> R1
if (item < 0)
NUMNEG++;
}

## Slide 152: Example 3
TTL GetNumNegatives
AREA MyProgram, CODE, READONLY ; start of code
ENTRY
Main
LDR R0, N ; R0 = counter
LDR R1, =ARR ; R1 = pointer to table
MOV R2, #0 ; R2 = number of negatives
LOOP LDR R3, [R1], #4 ; R3 = current item, update pointer
CMP R3, #0 ; Compare item and 0
ADDLT R2, R2, #1 ; Add if item <0
SUBS R0, R0, #1 ; decrement counter
BNE LOOP ; check if all items have been processed
STR R2, RESULT ; Store result to M[RESULT]
HERE BAL HERE ; end of code
AREA Data1, DATA, READWRITE
N DCD 5
ARR DCD -2, 9, 121,-222, 5
RESULT DCD 0
END

## Slide 153: SIMULATION USING KEIL uVISION (EXTRA)

## Slide 154: Verifying your code through a Simulator
A simulator is a software which models an actual hardware
System developers always perform simulations to verify their codes before implementing it in hardware.
For ARM, we will be using Keil MicroVision (www.keil.com)
Keil Microvision is one of the best simulators for ARM processor.
Acquired by ARM in October 2005
Includes C/C++ compilers, debuggers, integrated environments, simulation models, and evaluation boards for ARM, Cortex-M, Cortex-R, 8051, C166, and 251 processor families.

## Slide 155: Step 1: Download the emulator
The software can be downloaded from http://www.keil.com/demo/
Select ARM Evaluation Software.
Fill up your contact information…
Download the software and install it on your home PC.
Size of installer ~319MB.

## Slide 156: Step 2: Create your project
Select Project - New Project from the µVision4 menu. This opens a standard Windows dialog, which prompts you for the new project file name.
Create a new folder Add in your preferred destination directory.
Switch to the new folder and type the project name Add. µVision4 automatically adds the extension .uvproj.
Click Save.
Note: Use a separate folder for each project.

## Slide 157: Step 3: Select Device
Select the microcontroller you use. For our tutorials, choose ARM > ARM 7 (Big Endian)

## Slide 158: Step 4: Write your assembly code
Create your file: Go to File - New menu. This opens an empty editor window where you can enter your source code. µVision4 enables color syntax highlighting, when the file is saved with the extension *.S, *.C or *.CPP.
Save the file using File - Save As..., and name it, e.g. , add.s. The extension .s is an assembly code file.
Write the code in the text editor
Add the file to your project. Invoke the Context Menu of the Source Group 1 in the Project Window (shown in the left Figure)
The navigation panel should look like this

## Slide 159: Step 5: Setting the environment
To run the program, your program needs to be loaded into the main memory.
Different locations may be assigned for the code and data area, depending on your setup.
In the simulation environment of uVision, this can be set.
In a physical environment, this is determined by the hardware setup.
LDR R1, A
LDR R2, B
ADD R1, R1, R2
STR R1, C
HERE BAL HERE
Memory
0x0000000A
0x00000014
0x00000000
A
B
C
Code AREA (PROGRAM)
Data AREA (Data1)

## Slide 160: Step 5: Setting the environment
Right-click on Target 1 in the navigational panel and select ‘Options for target ‘Target 1’’
The options menu box will pop up. Goto Linker. For our classes, we shall follow the following setup for all our tutorials.
Use separate regions for the code and data.
  Set R/O Base to 0x00000000 to define the code area
  Set R/W Base to 0x00001000 to define the data area
  Put an extra parameter --split at misc controls (double hyphen)
Source: http://www.keil.com/support/man/docs/armlink/armlink_Cacbdbbc.htm

## Slide 161: Step 6: Assembling your program
Assemble and link the source files of the application by clicking on one of the build-buttons located in the Build Toolbar.
If there are errors, they will be displayed in the Build Output Window. Double-click to jump to the error line. Correct the error and recompile.
Important: Remember to re-build your program after you make changes to your source code!!!
With Error
Without Error

## Slide 162: Debugging Using the .O and .LST File
After assembling your program, three important file will be created in your project directory:
.o file which stores the machine code/binary to be stored in the memory
.lst file is a file which shows the result of assembled machine code arranged line by line with your assembly code. This file is created for your debugging purposes only.
The memory for both code and data is not absolute . They have to be added to a base address:
R/O base: 0x0000 0000
R/W base: 0x0000 1000
Memory Location
(not absolute)
Assembly Code
Machine
Code

## Slide 163: MAP File
After assembling your program, three important file will be created in your project directory:
.o file which stores the machine code/binary to be stored in the memory
.lst file is a file which shows the result of assembled machine code arranged line by line with your assembly code. This file is created for your debugging purposes only.
.map file which shows the absolute address of the code and data area.
- Memory map specifies where the code and data section is loaded in the memory

## Slide 164: MAP File
After assembling your program, three important file will be created in your project directory:
.o file which stores the machine code/binary to be stored in the memory
.lst file is a file which shows the result of assembled machine code arranged line by line with your assembly code. This file is created for your debugging purposes only.
.map file which shows the absolute address of the code and data area.
  - Memory map specifies where the code and data section is loaded in the memory
  - Symbol table specifies the absolute address of each variable

## Slide 165: Step 7: Running and Debugging
Debugging is one of the most important skill you need to acquire when writing programs. If you do not know how to debug your program, you have not really master programming.
The debugging windows allows you to do the following
    Step through your program line-by-line. From here, we can check if the execution flow of your code is according to what you expect the program to do. If it doesn’t, you can pinpoint what is wrong with your code.
    Monitor the values of the registers. From here, we can monitor if the register has been updated correctly.
    Monitor the values of the specified memory. From here, we can monitor if the memory is being updated/loaded correctly.
Click Debug > Start/Stop Debug Session (or Ctrl-F5) to start debugging

## Slide 166: Step 7: Running and Debugging
Registers window shows you the value of the content of the registers during execution including the Program Counter or PC (R15) and the Status Register or CPSR.
Current value of PC = 0x0 (start of program)

## Slide 167: Step 7: Running and Debugging
Code Window shows your assembly code. The yellow arrow shows the next instruction to be executed.

## Slide 168: Step 7: Running and Debugging
Disassembly Windows shows the assembly code and its corresponding machine code and the relative (not absolute) address of each code.
The yellow arrow points to the next instruction to be executed which is corresponding to the Program Counter (PC) value shown in the Register Window.

## Slide 169: Step 7: Running and Debugging
Memory Windows shows the content of the memory at the specified location. Normally, we would like to view the content as unsigned integer. To change the settings for the view mode,
Right click on the bar on the right of the address, and select Unsigned > Int
Make sure the Decimal option is NOT checked.

## Slide 170: Step 7: Running and Debugging
Memory Windows
Type the address you are interested to observe its content
…
AREA Data1, DATA, READWRITE ; start of data
A DCD 0x0000 000A DCD 0x0000 0014
C DCD 0
From the map file (.map):
Assembly code (.s)
Memory content:

## Slide 171: Step 7: Running and Debugging
To run an instruction, press F10 or press the Step-Into/Step-Through Button. Yellow line indicates next instruction to run.
Instruction #1: LDR R1, A
R1 is updated with the value pointed by A
R1  [A] where A = 0x00001000 and [A] = 0xA
PC  PC + 4 = 0x4 (points to the next instruction)

## Slide 172: Step 7: Running and Debugging
To run an instruction, press F10 or press the Step-Into/Step-Through Button
Instruction #2: LDR R2, B
R2 is updated with the value pointed by B
R2  [B] where B=0x00001004 and [B] = 0x14
PC  PC + 4 = 0x8

## Slide 173: Step 7: Running and Debugging
To run an instruction, press F10 or press the Step-Into/Step-Through Button
Instruction #3: ADD R1, R1, R2
R1  R1 + R2 (10 + 20) = 30
PC  PC + 4 = 0xC

## Slide 174: Step 7: Running and Debugging
To run an instruction, press F10 or press the Step-Into/Step-Through Button
Instruction #3: ADD R1, R1, R2
R1  R1 + R2 (10 + 20 = 30
PC  PC + 4 = 0xC
Instruction #4: STR R1, C
[C]  R1
PC  PC + 4 = 0x10