## Slide 1: UECS1013 Introduction to Computer Organisation and Architecture
Lecture 2

## Slide 2: Outline: Number System
  Conversion Between Number Systems
    Conversion from Decimal (Base 10) to other Bases
    Sum of Weights Technique
    Radix Divide and Multiply Technique
    Special Conversion Cases: Related Number Bases
  Manual Arithmetic in Different Number Bases
    Addition
    Multiplication
    Subtraction
    Division
  Computational Arithmetic
    Sign and Magnitude
    9’s and 10’s Decimal Complement
    1’s and 2’s Binary Complement

## Slide 3: CONVERSION BETWEEN NUMBER SYSTEMS

## Slide 4: Conversion from Decimal (Base 10) to Other Bases
There are two different methods to perform conversion from Decimal (Base 10) to other bases:
Method 1: Sum of Weights Technique
Method 2: Radix Divide and Multiply Technique
  Repeated division for integral part
  Repeated multiplication for fractional part

## Slide 5: Sum of Weights
[Recap] Converting a number (base 8) to base 10
Converting from base 10 to another base
  Use the same method in reverse (not so simple)
  Method: Find the values at each position each with different weights such that the total will add up to the base 10 number that we are trying to convert
Number = 137548
Value  1 3 7 5 4 8 Weight  4096 512 64 8 1
Number = 4096 + 1536 + 448 + 40 + 4
= 612410

## Slide 6: Sum of Weights
Position | 5 | 4 | 3 | 2 | 1 | 0 | -1 | -2
Weight (Base 2) | 32 | 16 | 8 | 4 | 2 | 1 | 0.50 | 0.25
Division |  |  |  |  |  |  |  | 
Quotient |  |  |  |  |  |  |  | 
Remainder |  |  |  |  |  |  |  | 
28.7510
Integral Part
Step1: Start from the first position from the left with a weight smaller than the decimal number.
Step2: Divide the remainder (initially the integral part of the original number) by the current weight to generate the remainder and quotient.
Step3: Go to next position and repeat step 2 until the first integral digit.
The value at the quotient is our result
Fractional Part
Repeat step1 to step 3 but for fractional part
12/8
4
1
4/4
0
1
0/2
0
0
0/1
0
0
28/16
12
1
= 11100.112
0.25/0.25
0
1
0.75
/0.5
0.25
1

## Slide 7: Sum of Weights
Example: Convert 612410 to Base 5
Position | 6 | 5 | 4 | 3 | 2 | 1 | 0
Weight (Base 5) | 15625 | 3125 | 625 | 125 | 25 | 5 | 1
Division |  | 6124/ 3125 | 2999/ 625 | 499/ 125 | 124/ 25 | 24/5 | 4/1
Quotient |  | 1 | 4 | 3 | 4 | 4 | 4
Remainder |  | 2999 | 499 | 124 | 24 | 4 | 0
612410 = 143,4445

## Slide 8: Sum of Weights
Example: Convert 319310 to binary
Position Weights Division Quotient Remainder
12 4096
11 2048 3193/2048 1 1145
10 1024 1145/1024 1 121
9 512 0
8 256 0
7 128 0
6 64 121/64 1 57
5 32 57/32 1 25
4 16 25/16 1 9
3 8 9/8 1 1
2 4 0 1
1 2 0 1
0 1 1/1 1 0
Answer: 319310 = 1100011110012

## Slide 9: Radix Divide and Multiply
Division-by-Base (Base 2 example)
For the integral part, write down a sequence of bits, determined by the following procedure, to the left of the radix point:
  Divide the number by 2.
  If the result in non-integral, write down a 1. Otherwise write down a 0.
  Retain the integral part of the result.
  If it is non-zero, go back to step 1 and keep writing to the left of the previously written sequence.

## Slide 10: Radix Divide and Multiply
Multiplication By Base (Base 2 example)
For the fractional part, write down a sequence of bits, determined by the following procedure, to the right of the radix point:
  Multiply the number by 2.
  If the integral part of the result is 1, write down a 1. Otherwise write down a 0.
  Retain the fractional part of the result.
  If it is non-zero, go back to step 1 and keep writing to the right of the previously written sequence.

## Slide 11: Radix Divide and Multiply
Example: Convert decimal number 28.625 into a binary number.
    28/2 = 14.0  0.
    14/2 = 7.0  00.
    7/2 = 3.5  100.
    3/2 = 1.5  1100.
    1/2 = 0.5  11100.
    0.625  2 = 1.25  .1
    0.25  2 = 0.5  .10
    0.5 x 2 = 1.0  .101
  Therefore, 28.7510 = 11100.1012.
Will the procedure always stop? Try 0.210
Example: Convert 13.70510 to binary.
Integral part: append to the left
Fractional part: append to the right

## Slide 12: Radix Divide and Multiply
Example:
Convert 250.2510 to hexadecimal
250 / 16 = 15 remainder of 10  A
15 / 16 = 0 remainder of 15  F
0.25  16 = 4.00  4
The result = FA.416
Convert 90.062510 to Octal
90 / 8 = 11 remainder of 2  2
11 / 8 = 1 remainder of 3  3
1/8 = 0 remainder of 1  1
0.0625  8 = 0.5  0
0.5 x 8 = 4.0  4
The result = 132.048

## Slide 13: Special Conversion Cases: Related Number Bases
Binary (k=1) | Octal (k=3) | Decimal | Hexadecimal (k=4)
0 000 | 0 | 0 | 0
0 001 | 1 | 1 | 1
0 010 | 2 | 2 | 2
0 011 | 3 | 3 | 3
0 100 | 4 | 4 | 4
0 101 | 5 | 5 | 5
0 110 | 6 | 6 | 6
0 111 | 7 | 7 | 7
1 000 | 10 | 8 | 8
1 001 | 11 | 9 | 9
1 010 | 12 | 10 | A
1 011 | 13 | 11 | B
1 100 | 14 | 12 | C
1 101 | 15 | 13 | D
1 110 | 16 | 14 | E
1 111 | 17 | 15 | F
The family of base 2k number systems is basically compatible with each other.
One complete permutation of 3 binary digits ≡ one complete round of octal set 08 to 78
One complete permutation of 4 binary digits ≡ one complete round of hexadecimal set 016to F16
Conclusion: conversion between base 2k number systems can be easily performed by grouping the digits

## Slide 14: Special Conversion Cases: Related Number Bases
Hexadecimal to Binary Conversion
  Convert 47.FE16 to binary
    4 7 . F E
    0100 0111 . 1111 1110
    47.FE16 = 0100 0111 . 1111 11102
Binary to Hexadecimal Conversion
  Convert 10010.0110112 to hexadecimal
    0001 0010 . 0110 1100
    1 2 . 6 C
    10010.0110112 = 12.6C16

## Slide 15: Special Conversion Cases: Related Number Bases
Octal to Binary Conversion
  Convert 47.128 to binary
    4 7 . 1 2
    100 111 . 001 010
    47.128 = 10 0111.0010 10002
Binary to Octal Conversion
  Convert 10010.0110112 to octal
    010 010 . 011 011
    2 2 . 3 3
    10010.0110112 = 22.338

## Slide 16: Special Conversion Cases: Related Number Bases
Hexadecimal to Octal Conversion
  Step 1: Convert Hex (or Octal) to binary
  Step 2: Convert from binary to Octal (or Hex)
Example:
  Convert 47.128 to hexadecimal
    4 7 . 1 28
    100 111 . 001 0102 (Convert to binary)
    10 0111. 0010 10002 (Regroup bits)
    2 7. 2 816 (Convert to hex)

## Slide 17: Review Questions
Convert the following number into Base 10.
  16AF16
Convert the following the following numbers into base 2
25.610
Convert the following the numbers into base 2
  6A16, 178
Convert the following the numbers into base 16
  1111 10112, 678

## Slide 18: Review Questions
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
2 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
3 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
4 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
5 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
6 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
7 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
8 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
9 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
The table contains the answer when adding two single digits
Example: 310 + 610 = 910 is given by the intersection of row 3 and column 6
Addition of two single digits may generate a two digit result, e.g. ,
510 + 810 = 1310 where 1 is the carry digit and 3 is the sum digit
Addition of multiple digits will be handled later.
Base 10 Addition Table

## Slide 19: MANUAL ARITHMETIC IN DIFFERENT NUMBER BASES

## Slide 20: Addition In Different Number Bases
 | 0 | 1
0 | 0 | 1
1 | 1 | 10
Base 2 addition table
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 10
2 | 2 | 3 | 4 | 5 | 6 | 7 | 10 | 11
3 | 3 | 4 | 5 | 6 | 7 | 10 | 11 | 12
4 | 4 | 5 | 6 | 7 | 10 | 11 | 12 | 13
5 | 5 | 6 | 7 | 10 | 11 | 12 | 13 | 14
6 | 6 | 7 | 10 | 11 | 12 | 13 | 14 | 15
7 | 7 | 10 | 11 | 12 | 13 | 14 | 15 | 16
Base 8 addition table
38 + 68 = 118
equivalent to
310 + 610 = 910
12 + 12 = 102 equivalent to 110 + 110 = 210

## Slide 21: Addition In Different Number Bases
Base 16 addition table
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10
2 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11
3 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12
4 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13
5 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14
6 | 6 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15
7 | 7 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16
8 | 8 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
9 | 9 | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
A | A | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
B | B | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A
C | C | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B
D | D | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B | 1C
E | E | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B | 1C | 1D
F | F | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 1A | 1B | 1C | 1D | 1E
E16 + D16 = 1B16 or equivalently 1410+1310 = 2710

## Slide 22: Addition In Different Number Bases
Method 1: By using the addition table
1 2 3
D E F
Carry
1
2
1
0
E
Sum
+
Carry
Sum
+
0
2
0
1
F
From addition table:
316 + F16 = 1216  1: carry, 2: sum
216 + E16 = 1016  1: carry, 0: sum
116 + D16 = 0E16  0: carry, E: sum
216  0: carry, 2: sum
116 + 016 = 116  0: carry, 1: sum
116 + E16 = F16  0: carry, F: sum
0
0
12316 + DEF16 = F1216

## Slide 23: Addition In Different Number Bases
Find 1 0010 00112 + 1101 1110 11112
1 0 0 1 0 0 0 1 1
1 1 0 1 1 1 1 0 1 1 1 1
Extending the power table to 3 variables:
Recommended for adding two binary numbers.
+
1
0
Carry
Sum
1
1
1
0
1
0
0
1
1
0
1
0
1
0
1
1
1 1 1
1
1
+1
1
1
0 0 0 0
Method 2: By using an extended addition table
Augend
Addend

## Slide 24: Multiplication In Different Number Bases
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
3 | 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27
4 | 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36
5 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
6 | 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54
7 | 0 | 7 | 14 | 21 | 28 | 35 | 42 | 49 | 56 | 63
8 | 0 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72
9 | 0 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81
Provides the result of multiplying two single digit numbers
Example: 310 x 610 = 1810
Product of multiple digits will be handled later.
Base 10 Multiplication Table

## Slide 25: Multiplication In Different Number Bases
Base 2 Multiplication Table
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
2 | 0 | 2 | 4 | 6 | 10 | 12 | 14 | 16
3 | 0 | 3 | 6 | 11 | 14 | 17 | 22 | 25
4 | 0 | 4 | 10 | 14 | 20 | 24 | 30 | 34
5 | 0 | 5 | 12 | 17 | 24 | 31 | 36 | 43
6 | 0 | 6 | 14 | 22 | 30 | 36 | 44 | 52
7 | 0 | 7 | 16 | 25 | 34 | 43 | 52 | 61
Base 8 Multiplication Table
38 x 68 = 228 equivalent to 310 x 610 = 1810
(no digit 8 or 9, of course)
12 x 12 = 12
 | 0 | 1
0 | 0 | 0
1 | 0 | 1

## Slide 26: Multiplication In Different Number Bases
Base 16 Multiplication table
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | F
2 | 0 | 2 | 4 | 6 | 8 | A | C | E | 10 | 12 | 14 | 16 | 18 | 1A | 1C | 1E
3 | 0 | 3 | 6 | 9 | C | F | 12 | 15 | 18 | 1B | 1E | 21 | 24 | 27 | 2A | 2D
4 | 0 | 4 | 8 | C | 10 | 14 | 18 | 1C | 20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
5 | 0 | 5 | A | F | 14 | 19 | 1E | 23 | 28 | 2D | 32 | 37 | 3C | 41 | 46 | 4B
6 | 0 | 6 | C | 12 | 18 | 1E | 24 | 2A | 30 | 36 | 3C | 42 | 48 | 4E | 54 | 5A
7 | 0 | 7 | E | 15 | 1C | 23 | 2A | 31 | 38 | 3F | 46 | 4D | 54 | 5B | 62 | 69
8 | 0 | 8 | 10 | 18 | 20 | 28 | 30 | 38 | 40 | 48 | 50 | 58 | 60 | 68 | 70 | 78
9 | 0 | 9 | 12 | 1B | 24 | 2D | 36 | 3F | 48 | 51 | 5A | 63 | 6C | 75 | 7E | 87
A | 0 | A | 14 | 1E | 28 | 32 | 3C | 46 | 50 | 5A | 64 | 6E | 78 | 82 | 8C | 96
B | 0 | B | 16 | 21 | 2C | 37 | 42 | 4D | 58 | 63 | 6E | 79 | 84 | 8F | 9A | A5
C | 0 | C | 18 | 24 | 30 | 3C | 48 | 54 | 60 | 6C | 78 | 84 | 90 | 9C | A8 | B4
D | 0 | D | 1A | 27 | 34 | 41 | 4E | 5B | 68 | 75 | 82 | 8F | 9C | A9 | B6 | C3
E | 0 | E | 1C | 2A | 38 | 46 | 54 | 62 | 70 | 7E | 8C | 9A | A8 | B6 | C4 | D2
F | 0 | F | 1E | 2D | 3C | 4B | 5A | 69 | 78 | 87 | 96 | A5 | B4 | C3 | D2 | E1
E16 x D16 = B616 (1410x1310 = 18210)

## Slide 27: Multiplication In Different Number Bases
Find the product of two hex integers 123 and DEF
Step 1: Break down the second multiplier into single digits
123 x DEF = 123 x (D00 + E0 + F)
= (123 x D) x 100 + (123 x E) x 10+ (123 x F) x 1
Step 2: Find the product in parenthesis individually
Step 3: Sum up the individual products
123xDEF = EC7 x 100 + FEA x 10 + 110D
= EC700 + FEA0 + 110D = FD6AD
1 2 3
X D
2 7
1 A
D
E C 7
1 2 3
X E
2 A
1 C
E
F E A
1 2 3
X F
2 D
1 E
F
1 1 0 D

## Slide 28: Multiplication In Different Number Bases
Example: Find the product of two hex integers 123 and DEF
The three steps can be simplified into a single step as follows
1 2 3 Multiplicand
X D E F Multiplier
1 1 0 D (123xF)
F E A (123xE)
E C 7 (123xD)
F D 6 A D

## Slide 29: Multiplication In Different Number Bases
 |  |  | 1 | 1 | 0 | 1 | 
 |  |  |  | 1 | 0 | 1 | 
 |  |  | 1 | 1 | 0 | 1 | Position 0 (1st digit)
 |  |  | 0 | 0 | 0 |  | Position 1 (2nd digit)
 | 1 | 1 | 0 | 1 |  |  | Position 2 (3rd digit, first operand shifted by 2 bits)
1 | 0 | 0 | 0 | 0 | 0 | 1 | Add
Example: Find the product of two binary 1101 x 101
redundant

## Slide 30: Subtraction In Different Number Bases
Borrow |  | 0 | 10 0 | 01 10 | 01 10 |  | 10 0 | 2 |  |  | 
Minuend |  | 1 | 1 | 0 | 0 |  | 1 | 0 | 1 | 1 | 
Subtrahend | - | 0 | 1 | 1 | 0 |  | 1 | 1 | 1 | 0 | 
Result |  | 0 | 1 | 0 | 1 |  | 1 | 1 | 0 | 1 | 
Notes: Borrow, Minuend, Subtrahend and Result are expressed in the corresponding base (Base 2 in this example) |  |  |  |  |  |  |  |  |  |  | 
Similar to Base 10. However a borrow is required from its immediate left digit, the base value is borrowed.
Example: 1100 10112 – 0110 11102
Equals to 2 in Base 10

## Slide 31: Subtraction In Different Number Bases
Minuend |  | 1 | 0 | 1 | 1 |  | 0 | 1
Subtrahend | - | 0 | 1 | 1 | 0 |  | 1 | 0
 |  | 0 | 1 | 0 | 0 |  | 1 | 1
Example: 10 11012 – 01 10102
Example: 54758 – 37648
Borrow |  | 4 | 14 |  |  | 
Minuend |  | 5 | 4 | 7 | 5 | 
Subtrahend | - | 3 | 7 | 6 | 4 | 
 |  | 1 | 5 | 1 | 1 | 
Equals to 12 in Base 10

## Slide 32: Subtraction In Different Number Bases
Example: 245D16 – 15FC16
Borrow |  | 1 | 13 3 | 15 |  | 
Minuend |  | 2 | 4 | 5 | D | 
Subtrahend | - | 1 | 5 | F | C | 
 |  |  | E | 6 | 1 | 
Equals to 21 in Base 10
Equals to 19 in Base 10

## Slide 33: Division In Different Number Bases
Division of Z / Y where Z is the dividend and Y is the divisor
Steps are similar to Base 10:
  Align the divisor (Y) with the most significant end of Z. Let the portion of the dividend to its bit aligned with the LSB of the divisor be denoted as X.
  Compare X and Y.
    If X ≥ Y, the quotient digit is X/Y and perform X – Y.
    If X < Y, the quotient digit is 0
  Shift Y by ONE bit to the right and go to step 2.

## Slide 34: Division In Different Number Bases
 |  |  |  |  | 0 | 1 | 1 | 1 |  | Quotient |  | 
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 |  |  |  | 
 |  |  | 0 | 0 | 0 |  |  |  |  |  |  | 
 |  |  | 1 | 1 | 0 | 1 |  |  |  |  |  | 
 |  |  |  | 1 | 1 | 1 |  |  |  |  |  | 
 |  |  |  | 1 | 1 | 0 | 0 |  |  |  |  | 
 |  |  |  |  | 1 | 1 | 1 |  |  |  |  | 
 |  |  |  |  | 1 | 0 | 1 | 1 |  |  |  | 
 |  |  |  |  |  | 1 | 1 | 1 |  |  |  | 
 |  |  |  |  |  | 1 | 0 | 0 |  | remainder |  | 
Example: 1101012 / 1112

## Slide 35: Division In Different Number Bases
 |  |  | 0 | 6 | 2 |  | Quotient |  | 
 |  | 7 | 5 | 4 | 3 |  |  |  | 
 |  |  | 0 |  |  |  |  |  | 
 |  |  | 5 | 4 |  |  |  |  | 
 |  |  | 5 | 2 |  |  |  |  | 
 |  |  |  | 2 | 3 |  |  |  | 
 |  |  |  | 1 | 6 |  |  |  | 
 |  |  |  |  | 5 |  | Remainder |  | 
Example: 5438 / 78

## Slide 36: Division In Different Number Bases
 |  |  | 0 | 1 | E | C | Quotient |  | 
 |  | E | 1 | A | F | 3 |  |  | 
 |  |  | 0 |  |  |  |  |  | 
 |  |  | 1 | A |  |  |  |  | 
 |  |  | 0 | E |  |  |  |  | 
 |  |  |  | C | F |  |  |  | 
 |  |  |  | C | 4 |  |  |  | 
 |  |  |  |  | B | 3 |  |  | 
 |  |  |  |  | A | 8 |  |  | 
 |  |  |  |  |  | B | Remainder |  | 
Example: 1AF316 / E16

## Slide 37: Review Question
Perform the following operation
14768 + 35548 (answer = 52528)
1278 + 2916
Find the following operation
10011012 x 1001102
1E4A16 x FA216 (answer = 1D980D416)
Find the product of two hexadecimal numbers 2216 and 6716

## Slide 38: Review Question
Perform the following operation
5400458 – 3256548 (answer = 2121718)
54004516 – 32565416 (answer = 21A9F116)

## Slide 39: COMPUTATIONAL ARITHMETIC

## Slide 40: Representation for Signed Integers
How do computer represent negative numbers (signed numbers) and real numbers?
Numbers can be represented as a combination of
  Value or magnitude
  Sign (plus or minus)
To handle negative numbers, the following systems are used for signed numbers:
  2’s-complement (most commonly used)
  1’s-complement
  Sign-and-magnitude
To handle real numbers
  Floating Points (float, double)

## Slide 41: Sign and Magnitude (SM)
In daily usage, negative numbers are usually written by writing a minus sign in front.
  Example: - (12)10 , -(1100)2
In sign-and-magnitude representation, this sign is usually represented by a bit:
  0 represents + and 1 represents -
For example, a 4-bit number can have 1-bit sign and 3-bit magnitude.
  0010SM represents 2 for S&M
  1010SM represents -2 for S&M
Note that the same bit pattern (1010) have different value in SM and other representations
  1010SM represents -2 for S&M but 6 for unsigned binary
sign
magnitude

## Slide 42: Sign and Magnitude (SM)
The range of an n-bit number ranges from
-(2(n-1)-1) to +(2(n-1)-1)
For example, the range of numbers represented by a 4-bit number in SM is from
Largest Positive Number:
0 111 = +(7)10
Largest Negative Number:
1 111 = -(7)10
Two zeroes:
0 000 = +(0)10
1 000 = -(0)10
All the numbers that can be represented by 4-bit binary number in SM

## Slide 43: Sign and Magnitude (SM)
To negate a number, just invert the sign bit. For examples:
-01000012 = 1 0100001SM
-00001012 = 0 0000101SM
Difficulty in implementation: the actual methods of arithmetic used depends on the signs of the operands and the relative magnitudes of the inputs
4 + 2 vs 4 – 2 vs 12 - 4
Directly mimicking how human perform calculations does not makes a good machine due to the following reasons:
  Computer requires absolute definition of every possible condition. So, the algorithm must include every possibility
  Calculation algorithms are complex and difficult to implement in hardware

## Slide 44: The Methods of Complement
The method of complements is a technique used to perform subtraction using only addition.
Commonly used in modern computer and calculators
In a complement method,
  The first digit of the number represents a positive/ negative number
  The positive numbers remain untouched.
  The negative numbers are converted into its complement version.
  To subtract/add two numbers, simply add the two numbers.
Examples:
  9’s Complement in Decimal and equivalently the 1’s Complement in Binary
  10’s Complement in Decimal and equivalently the 2’s Complement in Binary

## Slide 45: 9’s Decimal Complement
Assume a three digit decimal (Base 10) number. Split the decimal into half.
Positive numbers:
  0 to 499 are considered positive and they will represent itself
Negative numbers:
  To assign a value to the negative numbers, allow each digit to be subtracted from the largest numeral in the radix. In the case of decimal, the largest value numeral is the digit 9.
    -110 is represented as (9-0=9, 9-0=9, 9-1=8  9989s)
    -49910 is represented as (9-4=5, 9-9=0, 9-9=0  5009s)
  Subtracting a value from some standard base value is known as taking the complement of the number.

## Slide 46: 9’s Decimal Complement
How to determine if a number is positive/negative?
By looking at the first digit
0 through 4  positive number
  5 through 9  negative number
There are two ways to represent the value 0 in 9’s complement:
9999s and 09s
Numbers | Negative |  | Positive | 
Range of Decimal numbers | -499 | -000 | +0 | 499
– Increasing value +
Representation method | Complement |  | Number itself | 
Calculation | 999 minus number |  | none | 
9’s Representation | 500 | 999 | 0 | 499

## Slide 47: 9’s Decimal Complement
To convert a positive decimal number N into 9’s representation,
  N10 is represented as N9s
To convert a negative decimal number N into 9’s representation, we take its complement by subtracting a value from a standard basis value. Given a number N with n digits, its negation or -N when represented as 9’s complement is defined as:
-N10 is represented as (10n-1– N)9s
To convert a positive 9’s representation number M (most significant digit <5) back to its decimal equivalent
M9s is represented as M10
To convert a negative 9’s representation number M (most significant digit >=5) M back to its decimal equivalent
M9s is represented as -(10n-1– M9)10 or
M9s is represented as (M9 - (10n-1))10

## Slide 48: 9’s Decimal Complement
Example: Convert the following decimal numbers into their 3 digits 9’s complement representation:
  45910 = 4599s (Positive number remains unchanged)
  -45910 = (103-1) – 459 = 999 – 459 = 5409s
Example: Convert -3610 into its 3 digits and 5 digits 9’s complement representation:
  -3610 = (102-1) – 36 = 99 – 36 = 639s
  -3610 = (105-1) – 36 = 99999 – 36 = 999639s
Example: Convert the following 9’s representation into their decimal value:
  4599s = 45910 (Positive number remains the same)
  5409s = 540 - (103-1) = 540 - 999 = -45910

## Slide 49: 9’s Decimal Complement
Steps to perform Addition/subtraction in 9’s complement
Convert all the decimal operands into its 9’s complement equivalent
  If the #digits is specified, then extend the number of digits to the targeted number of digits
  For example, perform 119 – 20 in 4 digit, 9’s complement
  11910  01199s
  -2010  99799s
  If the #digits in the operation is not specified, then the number of digits follows the larger digits.
    For example, perform 119 – 20 in 9’s complement
  11910  1199s
  -2010  9799s

## Slide 50: 9’s Decimal Complement
Steps to perform Addition/subtraction in 9’s complement (cont…)
  If the #digits in the operation is outside of the supported range, then the operation cannot be performed
    For example, perform 919 – 20 in 3 digit, 9’s complement
    91910 is out of range of a 3 digit, 9’s complement representation
2. Perform the addition with end-around carry.
For example, 273 – 18
9’s complement
2 7 3
+ 9 8 1
1 2 5 4
1
2 5 59s
Base 10
2 7 3
- 1 8
2 5 510

## Slide 51: 9’s Decimal Complement
Base 10 |  |  | +250 |  |  |  |  | +250 |  | 
 | -499 | -350 |  | -100 | -0 | 0 | 170 |  | 420 | 499
9’s Complement | 500 | 649 |  | 899 | 999 | 0 | 170 |  | 420 | 499
 |  |  | +250 |  |  |  |  | +250 |  | 
Addition without an end-around carry
  Happens when the addition does not result in the changes in the sign.
  The addition in 9’s Complement does not cross the modulus (999 for a three digit 9’s complement representation)
170 +250
420
-350 +250
-100
NEGATIVE NUMBERS
649 +250
899
In 9’s C
Both in Base 10 and 9’sC
In Base 10
POSITIVE NUMBERS

## Slide 52: 9’s Decimal Complement
Base 10 |  |  |  | +300 |  |  | 
 | -499 | -200 | -000 |  | 0 | 100 | 499
9’s Complement | 500 | 799 | 999 |  | 0 | 100 | 499
 |  |  |  | +300 |  |  | 
Addition with end-around carry:
  The addition in 9’s C crosses the modulus
  Happens when the addition of a positive and a negative numbers generates a positive number.
  Add the carry digit to the result (ignore the carry digit)
799 + 300
1 099
+1
100
-200 + 300
100
In 9’s C
In Base 10

## Slide 53: 9’s Decimal Complement
 |  |  |  |  | -300 |  |  | 
Base 10 | -499 | -000 | 0 | 200 | 499 | -499 | -100 | -000
9’s Complement | 500 | 999 | 0 | 200 | 499 | 500 | 899 | 999
 |  |  |  |  | +699 |  |  | 
Subtraction
  9 – 10 is implemented in terms of addition of a positive and a negative number 9 + (-10)
  Count to the right (number of steps = 9’s complement of the number, e.g. 699 steps for -300) to subtract a number
  Subtraction will always generate a wraparound
200 -300
100
In Base 10
200 + 699
899
In 9’s C

## Slide 54: 9’s Decimal Complement
 |  |  |  | -2 |  |  |  | 
Base 10 | -499 | -199 | -000 | 0 | 499 | -499 | -201 | -000
9’s Complement | 500 | 800 | 999 | 0 | 499 | 500 | 897 | 999
 |  |  |  | +997 |  |  |  | 
Subtraction
-199 -2
-201
In Base 10
800 + 997
1 797
+1
798
In 9’s C

## Slide 55: Review Questions
Convert the following numbers into 9’s complement
362
-367
-177 (5 digits)
-479 (8 digits)
Add the 2 numbers below using the following method.
    41 – 25 (9’s complement)
    497 + 136 (9’s complement)
    998 – 13 (3 digits, 9’s complement)
    999 – 28 (5 digits, 9’s complement)

## Slide 56: 10’s Decimal Complement
Numbers | Negative |  | Positive | 
Range of decimal numbers | -500 | -001 | 0 | 499
Representation method | Complement |  | Number itself | 
Calculation | 1000 minus number |  | none | 
Representation example | 500 | 999 | 0 | 499
Problem with 9’s complement:
  Two representations for a single value 0
  Extra operations when end-around carry is required
10’s complement:
  One single representation for a single value 0
  No end-around carry required. The carry digit is simply ignored.

## Slide 57: 10’s Decimal Complement
Given a number N with n digits, its negation or -N when represented as 10’s complement is defined as:
9’s complement + 1 = (10n-1) – N + 1 = 10n-N
The positive number remains the same
Example: Find the 10’s complement of the following decimal numbers:
  459 = 45910c = 4599s (Positive number remains the same)
  -459 = 103 – 459 = 1000 – 459 = (541)10c
  -36 = 102 – 36 = 100 – 36 = (64)10c
  -36 (Use 5 digits) = 105 – 36 = 100000 – 36 = (99964)10c
Example: Convert from 10’s complement back to decimal:
  (459)10s = (459)10 (Positive number remains the same)
  (541)10s = 541- (103) = 541- 1000 = -(459)10

## Slide 58: 10’s Decimal Complement
Addition/subtraction in 10’s Decimal Complement
Example: 27310 – 1810
Convert all the decimal operands into its 10’s complement equivalent. The same rules for conversion as 9’s complement applies.
273 + (–018)  27310 = (273)9s
01810 = (103 - 018)10s = (982)10s
2. Perform the addition and ignore the carry digit
2 7 3
+ 9 8 2
1 2 5 5 (ignore carry)
2 5 510s
In 10’s
2 7 3
+ 9 8 2
1 2 5 510
In Base 10

## Slide 59: Review Questions
Example 1: Get the 10’s complement of
247
-328
Example 2: Find 3 and 5 digits 10’s complement representation of -28
Example 3: Find the signed value of the 10’s complement representation 777.

## Slide 60: 1’s Binary Complement
Without loss of generalization, in a 4-bit number system:
A positive integer, X, is represented as 0b2b1b0
Example: 310 = 00111s
A negative integer -X is represented aswhere represents the compliment of .
Example: -310 = -00112 = 11001s
The method can be extended to any arbitrary number of bits.
Example: Convert -6 into its 5 bit 1’s Complement equivalent
-6 = -001102 = -110011s
Figure: 1’s Complement of a 4 bit number

## Slide 61: 1’s Binary Complement
Note that the value of a 4 bit number in binary is not equivalent to actual value of the number in 1s Complement
  10002 is 8 in value but 10001s has a value of -7
Formally, the number represented -N has the bit pattern of (2n-1)-N where n is the number of bit. Try compare with 9’s C.
  Example: When N = 6, -N or -6 is represented by the bit pattern (24-1)-6 = 9 or 1001 in 1’s complement
The range that can be represented by n digits in 1’s complement is
-(2(n-1)-1) to +(2(n-1)-1)
  Example: The range of a 4 bit number is - (23-1) to (23-1)- 1 = -7 to 7

## Slide 62: 1’s Binary Complement
Examples (assuming 8-bit binary numbers):
(14)10 = (00001110)2 = (00001110)1s
-(14)10 = -(00001110)2 = (11110001)1s
-(80)10 = -( ? )2 = ( ? )1s

## Slide 63: 1’s Binary Complement
Algorithm for addition, A + B:
Perform binary addition on the two numbers.
Perform end-around carry: if there is a carry out of the MSB, add 1 to the result.
Algorithm for subtraction, A – B:
A – B = A + (–B)
Take 1s complement of B by inverting all the bits.
Perform the addition operation as the steps per above

## Slide 64: 1’s Binary Complement
Examples: 4-bit binary system
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
+5 0101
+ -5 + 1010
---- -------
-0 1111
---- -------
-2 1101
+ -5 + 1010
---- ------
-7 10111
---- + 1
------
1000
- 1 1110
- 2 + 1101
---- ------
-3 11011
---- + 1
------
1100

## Slide 65: 2’s Binary Complement
2’s Complement of a 4 bit number

## Slide 66: 2’s Binary Complement
As in previous method, the value of a 4 bit number in binary is not equivalent to actual value of the number in 1s Complement
  10002 is 8 in value but 10002s has a value of -8
Formally, the number represented -N has the bit pattern of 2n-N where n is the number of bit.
  Example: when N = 6, -N or -6 is represented by the bit pattern 24-6 = 10 or 10102s in 2’s complement
The range that can be represented by n digits in 1’s complement is
-2(n-1) to +(2(n-1)-1)
  Example: The range of a 4 bit number is -23 to (23-1)-1 = -8 to 7

## Slide 67: 2’s Binary Complement
Sign-and-magnitude and 1st complement systems have -0 (redundant)
The 2's complement system does not have -0.
The 2’s complement system yields the most efficient logic circuit implementation (most often used in computers).
The positive numbers are the same for all systems

## Slide 68: 2’s Binary Complement
Algorithm for addition, A + B:
  Perform binary addition on the two numbers.
  Ignore the carry out of the MSB (most significant bit).
Algorithm for subtraction, A – B:
A – B = A + (–B)
  Take 2s complement of B by inverting all the bits and adding 1.
  Add the 2s complement of B to A.

## Slide 69: 2’s Binary Complement
Examples: 4-bit binary system
+3 0011
+ +4 + 0100
---- -------
+7 0111
---- -------
-2 1110
+ -6 + 1010
---- -------
-8 11000
---- -------
+6 0110
+ -3 + 1101
---- -------
+3 10011
---- -------
+4 0100
+ -7 + 1001
---- -------
-3 1101
---- -------

## Slide 70: Carry and Overflow
Signed binary numbers are of a fixed range.
If the result of addition/subtraction goes beyond this range, overflow occurs.
In practice, we check the consistencies between sign bit to determine for overflow
  positive + positive gives negative  overflow
  negative + negative gives positive  overflow
  positive + negative will never cause overflow

## Slide 71: Carry and Overflow
Examples: 4-bit numbers (in 2s complement)
Range of number is (1000)2s to (0111)2s or (-810 to 710)
(0101)2s + (0110)2s = (1011)2s
(5)10 + (6)10 = -(5)10 ?! (overflow!)
(1001)2s + (1101)2s = (10110)2s discard end-carry
= (0110)2s (overflow!)

## Slide 72: Carry and Overflow
Example 1:
  4 bit, 4 + 2
  Correct result
  No overflow, no carry
Example 2:
  4 bit, 4 + 6
  Incorrect result
  Overflow, no carry
0100 | = | (+ 4)
0010 | = | + (+ 2)
0110 | = | (+ 6)
0100 | = | (+ 4)
0110 | = | + (+ 6)
1010 | = | (– 6)
Check if overflow happens for the following arithmetic computation

## Slide 73: Carry and Overflow
Example 3:
  4 bit, -4 + -2
  Result correct ignoring the carry
  Carry but no overflow
Example 4:
  4 bit, -4 + -6
  Incorrect result
  Overflow, carry ignored
1100 | = | (– 4)
1110 | = | + (– 2)
11010 | = | (– 6)
1100 | = | (– 4)
1010 | = | + (– 6)
10110 | = | (+ 3)

## Slide 74: Carry and Overflow
More examples: 4-bit binary system
Which of the above is/are overflow(s)?
Both (-9 and +11 is outside the range of a 4-bit binary 2nd complement system)
-3 1101
+ -6 + 1010
---- -------
-9 10111
---- -------
+5 0101
+ +6 + 0110
---- -------
+11 1011
---- -------

## Slide 75: Review Question
Perform the following arithmetic operations with binary numbers (7 bits) and 2’s complement representation. Check if overflow happens
(+35) + (+40)
(-35) + (-40)
Perform the following arithmetic operations in 4 bits, 2’s complement. Check if there are any overflows.
-3 - 6
5 + 6