## Slide 1: UECS1013 Introduction to Computer Organisation and Architecture
Lecture 3

## Slide 2: Outline: Number System
  Exponential Notation
    Exponential Notation in Decimal Format
      Conversion
      Addition and Subtraction
      Multiplication and Division
    IEEE Floating Point Standard
      Conversion
      Addition and Subtraction
      Precision
  Codes
    BCD
    Gray Code
    Self-Complementing Code
    Alphanumeric Code
    Error Detection Codes

## Slide 3: Exponential Notation
Also referred to as Scientific Notation
Used in computer when the number
  Is outside the integer range of the computer (too large or too small)
  Contains a decimal fraction
Scientific notation is used to represent a wider range of real numbers. Examples of scientific notation:
  Decimal: 6.02471023
  Binary: 1.10111 2-111

## Slide 4: EXPONENTIAL NOTATION IN BASE 10

## Slide 5: Exponential Notation in Decimal Format
Fixed point numbers are not sufficient for scientific calculations.
Scientific notation is used to represent a wider range of real numbers. Examples of scientific notation:
4 specifications required for a number
  Sign (“+” in example)
  Magnitude or mantissa (35790)
  Sign of the exponent (“-” in 10-6)
  Magnitude of the exponent (6)
Plus
  Base of the exponent (10)
  Location of decimal point (or other base) radix point
Sign of the mantissa |  | Sign of the exponent | 
 | -0.35790 x 10-6 |  | 
Location of decimal point | Mantissa | Base | Exponent

## Slide 6: Exponential Notation in Standard Floating Point Format
Predefined format, unless specified assumed to be 8 digits
  Digits are allocated for sign, exponent and mantissa
  Sign-&-magnitude format is used
  Increased range of values (two digits of exponent) will be traded for decreased precision (two digits of mantissa)
Mantissa: Assume decimal point located at beginning of mantissa
Sign: 0 represents +, 5 represents -
Sign of the mantissa | 
SEEMMMMMSF | 
2-digit Exponent | 5-digit Mantissa

## Slide 7: A Standard Floating Point Format
Representation | 0 | 49 | 50 | 99
Exponent being represented | -50 | -1 | 0 | 49
 | – Increasing value + |  |  | 
Exponent: Use Excess N notation where N is typically the middle value to be offset from the original exponent value.
  Example:
    The value of the exponent digits for
    0.22 x 1012 , excess 50 = 12 + 50 = 72
    0.22 x 10-12, excess 50 = -12 + 50 = 38
Possible for the number to be too large (overflow) or too small for representation (underflow)

## Slide 8: Conversion to Standard Format
Normalization is the process of shifting the numbers left or right until the integral part has a value of zero and the first digit of the fractional part is non-zero. To normalize a decimal number:
  Provide number with exponent (0 if not yet specified)
  Increase or decrease the exponent until the decimal point is at the right position.
  Correct precision by adding 0’s or discarding/rounding least significant digits
To convert a number into excess N decimal representation:
  Normalize the number
  Extract the mantissa value
  For positive number, the sign is 0. For negative number, the sign is 5.
  Convert the sign into its excess N form

## Slide 9: Conversion to Standard Format
1. Add exponent | 246.8035 x 100
2. Position decimal point | .2468035 x 103
3. Cut to 5 digits | .24680 x 103
4. Convert number | 05324680SF
Sign
Excess-50 exponent
Mantissa
Example 1: 246.8035

## Slide 10: Conversion to Standard Format
1. Exponential notation | 1255x 10-3
2. Position decimal point | 0.1255 x 10+1
3. Add 0 for 5 digits | 0.1255 x 10+1
4. Convert number | 05112550SF
1. Exponential notation | - 0.00000075 x 100
2. Position decimal point | - 0.75 x 10-6
3. Add 0 for 5 digits | - 0.75000 x 10-6
4. Convert number | 54475000SF
Example: - 0.00000075
Example: 1255 x 10-3

## Slide 11: Conversion Examples
245.67 | = | 0.24567 x 103 | = | 05324567SF
– 0.0010000 | = | – 0.10000 X 10-2 | = | 54810000SF
– 55555 | = | – 0.55555 x 105 | = | 5555555SF
0.025000 | = | 0.25000 x 10-1 | = | 04925000SF
?
?
?
?

## Slide 12: Floating Point Calculations
Addition and subtraction
  Exponent and mantissa treated separately
  Exponents of numbers must agree
    Align decimal points
    Least significant digits may be lost
  Mantissa overflow requires exponent again shifted right

## Slide 13: Addition and Subtraction
Add 2 floating point numbers | 0 51 99520 + 0 49 67850
Align exponents | 0 51 99520 0 51 0067850
Add mantissas; (1) indicates a carry | (1)0019850
Carry requires right shift | 05210019(850)
Round to get result | 05210020
Check results | 
05199520 = 0.99520 x 101 | = 9.9520
04967850 = 0.67850 x 101 | = 0.06785
 | = 10.01985
In exponential form | = 0.1001985 x 102
Perform the 05199520SF + 04967850SF

## Slide 14: Multiplication and Division
Mantissas: multiplied or divided
Exponents: added or subtracted
  Normalization necessary to
    Restore location of decimal point
    Maintain precision of the result
  Adjust excess value since added twice
    Example: 2 numbers with exponent = 3 represented in excess-50 notation
    53 + 53 =106
    Since 50 was added twice, subtract: 106 – 50 =56

## Slide 15: Multiplication and Division
Multiply 2 numbers | 0 52 20000 x 0 47 12500
Add exponents, subtract offset | 52 + 47 – 50 = 49
Multiply mantissas | 0.20000 x 0.12500 = 0.025000000 = 0.25 x 10-1
Normalize the results | Exponent = 49 – 1 = 48
Results | 04825000
Check results | 
05220000 = | 0.20000 x 102
04712500 = | 0.125 x 10-3
= | 0.0250000000 x 10-1
Normalizing and rounding = | 0.25000 x 10-2
Perform the 05220000SF x 04712500SF

## Slide 16: Review Exercise
The following decimal numbers are already in excess-50 floating point format. Add them. A 9 is used as a negative sign. Present your result in standard sign-and-magnitude form
05225731 + 04833300
05012500 + 95325750
05452500 x 04822200
96450000 x 94450000

## Slide 17: IEEE FLOATING POINT STANDARD

## Slide 18: IEEE Floating Point Standard
Sign of
number :
32 bits
mantissa fraction
23-bit
representation
excess-127
exponent in
8-bit signed
S
M
Value represented
E
¢
+
1.
M
2
E
¢
127
-
´
±
=
0 signifies
-
1 signifies
52-bit
mantissa fraction
11-bit excess-1023
exponent
64 bits
Sign
S
M
Value represented
1.
M
2
E
¢
1023
-
´
±
=
E
¢
A computer representation of the scientific notation:
Sign of the mantissa |  |  | 
 | -1.10111 x 2-111 |  | 
Radix point | Mantissa | Base | Exponent
Double
Precision:
Single
Precision:

## Slide 19: Converting to IEEE Standard Format
Exponent
The exponent is represented using Excess X
Used to represent positive and negative exponents
The exponent is shifted by the excess value. Typically, this is to ensure the most negative exponent value is shifted upwards to 0.
Example : Excess 127
  - 3  -3 + 127 = 124 or 011111002
  + 3  3 + 127 = 130 or 100000102
The excess-x representation enables efficient comparison of the relative sizes of two numbers.

## Slide 20: Converting to IEEE Standard Format
Exponent
Example, 4 bits, excess 7
Exponent Value | Exponent Value + 7 | Excess-7 Representation
-7 | -7+7 = 0 | 00002
-6 | -6+7 = 1 | 00012
-5 | -5+7 = 2 | 00102
-4 | -4+7 = 3 | 00112
… | … | …
5 | 5+7 = 12 | 11002
6 | 6+7 = 13 | 11012
7 | 7+7 = 14 | 11102
8 | 8+7 = 15 | 11112
    Without excess mode, the range of supported exponent value is:
0 to 15
    With excess 7, the range of supported exponent value is
    (0 - 7) to (15 – 7)
    or
    -7 to 8
To convert from value to Excess X
value + X
To convert from Excess X to value
value - X

## Slide 21: Converting to IEEE Standard Format
Mantissa
Mantissa stored in sign magnitude form, lies in the range 1  m < 2
Normalized mantissa with an implied 1 as the most significant bit (normalized as 1.xxxx form) except for 0.00
Example:
  1001 = 1.001 x 2011  001 is the mantissa

## Slide 22: Converting to IEEE Standard Format
Example 1: Convert 10010 into IEEE floating point representation (single precision)
10010 = 11001002 = +1.1001002  2610 = +1.100100  2110
mantissa = 1001 00 00000000000000000 (single precision)
exponent (excess 12710) = 0111 11112 + 1102 = 1000 01012
10010 = 0 100 0010 1 100 100 0 0000 0000 0000 00002

## Slide 23: Converting to IEEE Standard Format
Example 2: Convert -0.510 into IEEE floating point representation (single precision)
  -0.510 = -0.12 = -1.0  2-1
  mantissa = 00000000000000000000000 (single precision)
  exponent (excess 12710) = 0111 11112 - 12 = 0111 1110
  -0.510 = 1 011 1111 0 000 0000 0000 0000 0000 00002

## Slide 24: Review Exercise
Convert -12.7510 into an IEEE single floating point representation

## Slide 25: Precision of Floating Points
Precision of Floating Points
Chopping
  Truncated to the required precision length by introducing a consistent downward bias in the operation.
  For example, truncate to 3 bits
    For 0.b-1 b-2 b-3 000 to 0.b-1 b-2 b-3 111  0.b-1 b-2 b-3
    Error = 0 to 0.000111

## Slide 26: Precision of Floating Points
Precision of Floating Points
Rounding
  Round to the nearest (used in the IEEE FP Standard) n bits.
  Case 1: The extra bits amounts to more than one-half of the last representable bit position
    Add 1 to the last representable bit, i.e. (for n = 3), 0.b-1 b-2 b-3 1…1…  0.b-1 b-2 b-3 +0.001
    Examples (round to 3 digits):
    0.011100110  0.011 + 0.001 = 0.100
    0.100110001  0.100 + 0.001 = 0.101

## Slide 27: Precision of Floating Points
Precision of Floating Points
Rounding
  Round to the nearest (used in the IEEE FP Standard) n bits
  Case 2: The extra bits amounts to less than half of the last representable bit
    Drop all extra bits
    0.b-1 b-2 b-3 0…1…  0.b-1 b-2 b-3
    Examples:
    0.011000110  0.011
    0.100010001  0.100

## Slide 28: Precision of Floating Points
Precision of Floating Points
Rounding
  Round to the nearest (used in the IEEE FP Standard) n bits
  Case 3: The extra bits amounts to exactly half of the last representable bit
    Force the result to be even i.e. the value is rounded-up if the last representable bit is currently '1' and left alone if it is currently '0‘
    0.b-1 b-2 b-3 1 if b-3 = 1, then b-1 b-2 b-3 +0.001
    if b-3 = 0
    Examples (round to 3 digits):
    0.0111000  0.011 + 0.001 = 0.100
    0.1101000  0.110

## Slide 29: Review Exercise
Approximate the following binary floating point numbers into 4 bits in the IEEE FP rounding standards
1.100110002 x 2112
1.100110102 x 2112
1.100101002 x 2112
Repeat by truncating the numbers in the IEEE FP standards

## Slide 30: Addition and Subtraction of Floating Points
Addition and Subtraction
Choose the number with the smaller exponent and shift its mantissa right to make the exponents equal.
Perform operation on the mantissas and determine the sign of the result.
Normalize the resulting value, if necessary.
Example
2.9400×102 + 4.3100×104
= 0.0294×104 + 4.3100×104
= 4.3394×104

## Slide 31: Addition and Subtraction of Floating Points
Addition and Subtraction
Assuming the following format 1 bit for sign bit, 4 bits for exponent in excess 7, 3 bits for mantissa. Perform the following operations:
0 1001 110 + 0 0111 110.
0 1001 110 - 0 0111 110.
Truncate if necessary. Present your value in IEEE FP format

## Slide 32: Addition and Subtraction of Floating Points
Addition
Step 1: Get the value from IEEE FP format.
0 1001 110 = +1.1102 x 29-710 = +1.112 x 2210
0 0111 110 = +1.1102 x 27-710 = +1.112 x 2010
Step 2: Align the exponent
+1.112 x 2010  0.0112 x 2210
Step 3: Perform addition
1.112 x 2210 + 0.0112 x 2210 = 10.0012 x 2210 = 1.00012 x 2310
Step 4: Convert to IEEE FP
Exponent (Excess 7) = 3 + 7 = 10 = 1010
Mantissa = 000
Sign = 0
(0 1001 110)FP + ( 0 0111 110)FP = ( 0 1010 000)FP

## Slide 33: Addition and Subtraction of Floating Points
Subtraction
Borrow:
1 . 1 1 02 x 2210
- 0 . 0 1 12 x 2210
1 2
x 2210
210
0
210
0
1
1 . 0
1.112 x 2210 - 0.0112 x 2210 = 1.0112 x 2210
Step 3: Perform subtraction
Step 4: Convert back to FP IEEE format
Exponent (Excess 7) = 2 + 7 = 9= 1001
Mantisa = 011
Sign = 0
(0 1001 110)FP - ( 0 0111 110)FP = ( 0 1001 011)FP

## Slide 34: CODES

## Slide 35: Codes
Decimal numbers are more natural to humans. Binary numbers are natural to computers. Quite expensive to convert between the two.
If little calculation is involved, we can use some coding schemes for decimal numbers:
  BCD
  Gray Code
  Self-Complementing Codes (Excess 3, 84-2-1, 2*421)
  Error-detection Codes (Bi-quinary, Parity)
To represent a text, we can use
  ASCII

## Slide 36: Binary Coded Decimal (BCD)
One such scheme is BCD, also known as the 8421 code.
Represent each decimal digit as a 4-bit binary code.
A decimal of N digits will generate a 4×N bit BCD code.
Example:
1 2 410 = 11111002
0001
0010
0100 bcd
=

## Slide 37: Binary Coded Decimal (BCD)
BCD is not equivalent to binary.
Example: (234)10 = (11101010)2
Some codes are unused, eg: (1010)BCD, (1011) BCD, …, (1111) BCD. These codes are considered as errors.
Easy to convert, but arithmetic operations are more complicated.
Suitable for interfaces such as keypad inputs and digital readouts.

## Slide 38: Binary Coded Decimal (BCD)
Examples:
(234)10 = (0010 0011 0100)BCD
(7093)10 = (0111 0000 1001 0011)BCD
(1000 0110)BCD = (86)10
(1001 0100 0111 0010)BCD = (9472)10

## Slide 39: The Gray Code
Unweighted (not an arithmetic code).
Only a single bit change from one code number to the next.
Good for error detection.
Q. How to generate 5-bit standard Gray code?
Q. How to generate n-bit standard Gray code?

## Slide 40: The Gray Code
0
1
How to ensure only one bit changes between two adjacent numbers?
From 2 rows to 4 rows
Write the first 2 rows
Flip 2 rows vertically
Set the 2nd bit of the two
new rows to 1
From 4 rows to 8 rows
4. Generate the new 4 rows by flipping
the first 4 rows vertically
5. Set the 3rd bit of the new four rows to 1
Repeat the same procedure for the remaining rows
0
1
1
0
00
01
11
10
00
01
11
10
10
11
01
00
000
001
011
010
110
111
101
100
000
001
011
010
110
111
101
100
100
101
111
110
010
011
001
000
0000
0001
0011
0010
0110
0111
0101
0100
1100
1101
1111
1110
1010
1011
1001
1000
1
2
3
4
5

## Slide 41: The Gray Code
1 0 1
1 1 1
0 0 0
1 0 0
0 1 0
0 0 1
0 1 1
1 1 0
mis-aligned sensors
Gray coded: 111  101
Binary coded: 111  110  000
0 0 0
1 1 1
0 1 0
0 0 1
1 0 1
0 1 1
1 0 0
1 1 0
mis-aligned
sensors
0
1
2
3
4
5
6
7
There are many applications where only one bit changes for sequential data, e.g. counter

## Slide 42: Binary-to-Gray Code Conversion
Retain most significant bit.
From left to right, add each adjacent pair of binary code bits to get the next Gray code bit, discarding carries.
Example: Convert binary number 10110 to Gray code.
(10110)2 = (11101)Gray
The Gray Code

## Slide 43: Gray-to-Binary Conversion
Retain most significant bit.
From left to right, add each binary code bit generated to the Gray code bit in the next position, discarding carries.
Example: Convert the gray code 11011 to binary.
(11011)Gray = (10010)2
The Gray Code

## Slide 44: Other Decimal Codes
Self-complementing codes: excess-3, 84-2-1, 2*421 codes.
Error-detecting code: biquinary code (bi=two, quinary=five).

## Slide 45: Self-Complementing Codes
Examples: excess-3, 84-2-1, 2*421 codes.
The codes that represent the pair of complementary digits are complementary of each other.
0: 0011
1: 0100
2: 0101
3: 0110
4: 0111
5: 1000
6: 1001
7: 1010
8: 1011
9: 1100
241: 0101 0111 0100
758: 1010 1000 1011
Excess-3
binary-coded
Number:

## Slide 46: Alphanumeric Codes
Apart from numbers, computers also handle textual data.
Character set frequently used includes:
  alphabets: ‘A’ .. ‘Z’, and ‘a’ .. ‘z’
  digits: ‘0’ .. ‘9’ (not integer 0 to 9)
  special symbols: ‘$’, ‘.’, ‘,’, ‘@’, ‘*’, …
  non-printable: SOH, NULL, BELL, …
Usually, these characters can be represented using 7 or 8 bits.

## Slide 47: Alphanumeric Codes
ASCII: 7-bit, plus a parity bit for error detection (odd/even parity).

## Slide 48: Alphanumeric Codes
ASCII table:

## Slide 49: Error Detection Codes
Errors can occur data transmission. They should be detected, so that re-transmission can be requested.
With binary numbers, usually single-bit errors occur.
  Example: 0010 erroneously transmitted as 0011, or 0000, or 0110, or 1010.
Biquinary code uses 3 additional bits for error-detection. For single-error detection, one additional bit is needed.

## Slide 50: Error Detection Codes
Parity bit.
  Even parity: additional bit supplied to make total number of ‘1’s even.
  Odd parity: additional bit supplied to make total number of ‘1’s odd.
Parity bits
Odd parity

## Slide 51: Error Detection Codes
Parity bit can detect odd number of errors but not even number of errors.
  Example: For odd parity numbers,
  10011  10001 (detected)
  10011  10101 (non detected)
Parity bits can also be
applied to a block of data:
Column-wise parity
Row-wise parity

## Slide 52: Error Detection Codes
Sometimes, it is not enough to do error detection. We may want to do error correction.
Error correction is expensive. In practice, we may use only single-bit error correction.
Popular technique: Hamming Code (not covered).

## Slide 53: Review Questions
Change the decimal value below to BCD :-
  782, 190, 372
Convert between gray code and binary without referring to the conversion table
01002, 11002, 0100gray, 1100gray
Generate the (even) parity bits for the following data block. What is the impact of using error-detection codes?