## Slide 1: UECS2103 Operating Systems

## Slide 2: Contact
Mr. Sor Kean Vee
sorkv@utar.edu.my
016-2927502
Room: Level 8, FE33(1) Zone 1

## Slide 3: Main Reference
Operating Systems: Internals and Design Principles, 8th Ed. William Stallings, Prentice Hall

## Slide 4: Additional References
Operating System Design - The Xinu Approach. (2nd ed.). CRC Press. D. Comer. (2015).
Modern operating systems. (4th ed.). Pearson. Tanenbaum, A. S. (2014).

## Slide 5: Assessment
Coursework 40%
  Test 1 10%
  Test 2 10%
  Assignment 20%
Final exam 60%

## Slide 6: Tools
Virtual machine
  Vmware Workstation Player
    Latest version: https://my.vmware.com/en/web/vmware/free#desktop_end_user_computing/vmware_workstation_player/12_0
    Older version (Player 7): https://my.vmware.com/en/web/vmware/free#desktop_end_user_computing/vmware_player/7_0|PLAYER-714|product_downloads
  VirtualBox
    https://www.virtualbox.org/wiki/Downloads

## Slide 7: Tools
Image file (iso). Examples:
  https://www.ubuntu.com/download/desktop
  https://elementary.io/
  https://software.opensuse.org/422/en
  https://getfedora.org/en/workstation/download/

## Slide 8: Topics
Process Management
Scheduling
Memory Management
Secondary Storage Management
Security

## Slide 9: Basic Elements
Processor (CPU)
Main Memory (RAM) referred to as real memory or primary memory
I/O modules – move data between computer and its external environment
System bus - provides communication among processors, memory, and I/O modules

## Slide 10: Processor
PC : Program counter
IR : Instruction register
MAR : Memory address register
MBR : Memory buffer register
I/O AR : I/O address register
I/O BR : I/O buffer register

## Slide 11: Processor
PC - Contains the address of an instruction to be fetched
IR - Contains the instruction most recently fetched
MAR - Specifies the address for the next read or write
MBR - Contains data written into memory or receives data read from memory
I/O address register – specifies a particular I/O device
I/O buffer register – for exchanging data between I/O module and the processor

## Slide 12: Instruction Execution
Two steps
  Processor reads (fetches) instructions from memory (based on address stored in PC), one at a time, and placed in IR
  Processor executes each instruction
Instruction cycle – the processing required for a single instruction

## Slide 13: Instruction Execution
Action of an instruction can be categorised into
  Processor-memory - transfer data between processor and memory
  Processor-I/O - data transferred to or from a peripheral device
  Data processing - arithmetic or logic operation on data
  Control - alter sequence of execution

## Slide 14: Instruction Execution - Example

## Slide 15: Instruction Execution - Example
PC (Program Counter) contains 300, address of 1st instruction (in hexadecimal, 1940). The instruction is loaded into the instruction register (IR) and the PC increased by 1)

## Slide 16: Instruction Execution - Example
The 1st 4 bits (1st hexadecimal digit) indicate the AC to be loaded from memory (address 940, the remaining 12 bits or 3 hexadecimal digits)

## Slide 17: Instruction Execution - Example
Next instruction (5941) fetched and PC incremented.
Old contents of AC and contents of location 941 are added and result stored in AC.

## Slide 18: Instruction Execution - Example
Next instruction (2941) fetched and PC incremented.
Contents of AC are stored in location 941.

## Slide 19: Interrupts
Interrupt the normal sequencing of the processor to improve the utilisation of processor
Most I/O devices are slower than the processor
  Processor must pause to wait for device

## Slide 20: Interrupts
Program flow without interrupt

## Slide 21: Interrupts
Program flow with interrupt

## Slide 22: Interrupts
Processor checks for interrupts
  If no interrupts, fetch the next instruction for the current program
  If an interrupt is pending, suspend execution of the current program, and execute the interrupt-handler routine

## Slide 23: Interrupts
Interrupts classes

## Slide 24: Interrupts
Occurs after instruction at location N

## Slide 25: Interrupts
Return from interrupt

## Slide 26: Interrupts
Multiple interrupts
Priority: printer < disk < comm. line

## Slide 27: Operating System
A program that controls the execution of application programs
An interface between applications and hardware
Exploits the hardware resources of one or more processors
Provides services to system users
Manages secondary memory and I/O devices

## Slide 28: Operating System

## Slide 29: Operating System
Kernel
  Portion of operating system that is in main memory
  Contains most frequently used functions
  Also called the nucleus

## Slide 30: Operating System
Server operating system
Real-time operating system
Embedded operating system
Robot operating system
…